## Slide 1: Splitting FGI 3
Qualcomm, Ericsson, Nokia-Siemens Networks, ZTE, CATT
Nokia, Mediatek, LGE, ST-Ericsson, Renesas Technology Europe,
ATT, NTT DoCoMo, TeliaSonera, Deutsche Telekom
3GPP TSG RAN Meeting #50 RP-101430
Istanbul, Turkey, December 7 - 10, 2010 Agenda Item 8.2.2

## Slide 2: Splitting FGI 3: way forward
FGI 3 currently is:
  Semi Persistent Scheduling
  TTI bundling
  5-bit RLC Sequence Number & 7-bit PDCP Sequence Number
In order to facilitate introduction of features related to voice over LTE, the following is proposed
  Allow independent indication of support of SPS and of TTI bundling, without having dependency of one with the other
  Make the shorter RLC/PDCP sequence number mandatory for voice over LTE devices

## Slide 3: Splitting FGI 3: the way forward in practice
TTI bundling | Move to FGI 28 (newly created) & have no dependency on any other bit
Semi Persistent Scheduling | Move to FGI 29 (newly created) & have no dependency on any other bit
5-bit RLC & 7-bit PDCP Sequence Number | Keep in FGI 3 & set to TRUE for VoLTE capable devices & no dependency on any other bit
What happens to FGI 3? | FGI 3 meaning is changed (but no backward compatibility issues are envisaged in the real world)
It is also proposed to
  Realize the previously described changes in Release 9