## Slide 1: MBH IA Phase 3 – Joint Call with 3GPP
Bill Rembert, AT&T – Editor
Glenn Parsons, Ericsson
13 May 2013

## Slide 2: Outline
Introduction to MEF
Mobile CoS Phase 2 and Backhaul Phase 2
Introduction to Mobile Backhaul Phase 3 Project
  MBH Phase 3 Small Cell discussion examples

## Slide 3: Carrier Ethernet Defined
The MEF has defined Carrier Ethernet as
A ubiquitous, standardized, carrier-class Service and Network defined by five attributes that distinguish it from familiar LAN based Ethernet
Carrier Ethernet is often referred to in Enterprise circles as Ethernet Business Services. The MEF is the industry’s defining body for Carrier Ethernet.

## Slide 4: Carrier Ethernet Over Variety of Access Media
Carrier Ethernet provides consistent services delivered to users connected over the widest variety of access networks
MSO/ Cable
COAX
Direct Fiber
WDM Fiber
DS3/E3
Bonded Copper
Bonded T1/E1
Carrier 2
TDM
Ethernet
Ethernet
Ethernet
Ethernet
Ethernet
Ethernet
Ethernet
Direct Fiber
IEEE 802.3z, ae, G.8031, etc.
SONET/ SDH
PON Fiber
Ethernet
Ethernet
Ethernet
Ethernet over Packet Wireless
G.8032 Ethernet Ring
Ethernet
Carrier 1
UNI
ENNI

## Slide 5: CoS Phase 2: Performance Objectives by CoS Label
Example of Frame Delay (FD) oriented SLS, with FDR |  |  |  | 
Performance Metric | Parameters | Class of Service |  | 
 |  | H | M | L
Frame Delay (FD) | Objective (ms) | ≤10 | ≤ 20 | ≤ 37
 | Time Period (T) | 1 month | 1 month | 1 month
 | Percentile | 99.9 | 99 | 95
Frame Delay Range (FDR) | Objective (ms) | ≤ 5 | ≤ 10 | N/S
 | Time Period (T) | 1 month | 1 month | -
 | Percentile | 99.9 | 99 | -
Frame Loss Ratio | Objective (%) | ≤ .01 | ≤ .01 | ≤ .1
 | Time Period (T) | 1 month | 1 month | 1 month
Performance Tier 1 (PT1 - Metro)

## Slide 6: MBH Phase 2: Class of Service Mapping
CoS Name | Example of Generic Traffic Classes mapping into CoS |  | 
 | 4 CoS Model | 3 CoS Model | 2 CoS Model
Very High (H+) | Synchronization | - | -
High (H) | Conversational, Signaling and Control | Conversational and Synchronization, Signaling and Control | Conversational and Synchronization, Signaling and Control, Streaming
Medium (M) | Streaming | Streaming | -
Low (L) | Interactive and Background | Interactive and Background | Interactive and Background
Value to Mobile Operator: Know what performance each 3GPP traffic class will get
Value to MEN Operator: Standard CoS offering with default performance objectives
Notes: In addition to the ‘separate’ CoS, H+, for sync traffic class
MEF 23.x has specified 3 CoS Names: H/M/L – identified by specific PCP/DSCP values at the UNI.
Recommendation for Mobile Operator to map 3GPP service classes to these H/M/L CoS instances
Helps MO understand what performance each traffic class will get
Helps MEN operator to design network to support these standard CoS with default performance objectives.
6

## Slide 7: MBH IA Phase 3 Timeline
SB1 slipped, LB goal remains 4Q14
Rationale in backup
Develop and discuss foundational contributions (Alignment, Synch, MultiCEN, Small Cell, Performance)
2Q12 3Q12 4Q12 1Q13 2Q13 3Q13 4Q13 1Q14 2Q14 3Q14 4Q14
MBH Ph 3 project approval 2Q12
Working draft 1
Working draft 2
SB 1
SB 3 & AD2
SB 2 & AD1
LB
SB2 comment resolution
SB1 comment resolution
SB3 comment resolution
In addition to contributions, pre-SB comments are a very viable way to provide input and accelerate progress

## Slide 8: Review of Primary Scope Work Areas
Alignment
  MEF 6.x 10.3, 26.x, 33, etc as well as BBF, NGMN, etc
New Work Areas
    Areas are not independent. For example we are proceeding with Performance even though Synch contributions will likely impact. Note: no synch contributions so far.
  CoS/BWP (Performance)
    Addition of Availability, HLI, CHLI, FDR for H+
    BWP constraints and use cases
    Multi-MEN and MEF 23.2 dependency
  Multi-MEN
    EI and Service Attributes
    SOAM PM and FM
    CoS/BWP impacts including concatenation (see CoS/BWP)
    Synch impacts (see Synch)
  Small Cell /Het Net
    Develop and prioritize Use Cases
    EI and Service Attributes
    Inter-cell coordination
    Synch impacts including indoor/no GPS, tight coordination use cases (see Synch)
    CPO changes proposed for small cells, coordination impact
  Synch
    Synch across Multi-MEN (work frequency first, await ITU on Time/Phase)
    Frequency with packet method (await ITU response to New Metric liaison)
    Time and Phase with packet method for TDD LTE and some parts of LTE-A (also await ITU progress)

## Slide 9: Phase/time synchronization requirements by feature and service
Features |  | Time/Phase
WCDMA-TDD/LTE-TDD |  | +/-1.5 us
LTE eMBMS (LTE or LTE –A) | FDD and TDD | TBD
LTE-A eICIC | Inter-cell interference cancellation | TBD
LTE-A CoMP (Coordinated Multi-Point Transmission and Reception) | UL coordinated scheduling | TBD
 | DL coordinated scheduling | TBD
 | DL coordinated beamforming | TBD
 | DL non-coherent joint transmission | TBD
 | UL joint processing | TBD
 | UL selection combining | TBD
LTE-A cell cluster cooperation | ICIC and CoMP Joint Processing | TBD
Location Based Services (LBS) | OTDOA | TBD

## Slide 10: Small Cell BH Tight Coord Use Case
Mobile Network RAN BS site
Mobile Network RAN NC site
UNI
UNI
CEN
EVC(m)
RAN CE
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
Small Cell RAN BS site
UNI
UNI
CEN
EVC(sc)
RAN CE
UNI-C
UNI-C
UNI-N
UNI-N
New Performance requirements for Small Cell
with Tight Coordination Option
Existing Performance Tier 1 or 2

## Slide 11: DRAFT - Backhaul requirement for loose & tight radio coordination
LTE / LTE-A feature | Time synch common reference accuracy | Latency RTT | Bandwidth
Range expansion | None | None | Low
Adaptive resource partitioning | None | None | Low
Inter-Cell Interference Coordination (ICIC) | None | None | Low
eICIC (aka: ABS or Time Domain Partitioning) | +/- 5 us | None | Low
UL Coordinated Scheduling | +/- 5 us | 1-10 ms1 | Low
UL Coordinated link adaptation | None | 5-10 ms1 | Low
DL Coordinated Scheduling | +/- 5 us | 1-10 ms1 | Low
DL Coordinated link adaptation | None | 5-10 ms1 | Low
DL Coordinated beamforming | +/- 1.5 us | < 1 ms | 2.5-10 Gbps
DL non-coherent joint transmission | +/- 5 us | < 1 ms | < 150 Mbps
UL Joint processing | +/- 1.5 us | < 1 ms | 2.5-10 Gbps
UL Selection combining (aka: UL CoMP) | +/- 5 us | < 1 ms | < 150 Mbps
1 No strict requirement, performance benefit reduces with higher latency
None: Meaning no other requirements than the FDD or TDD system as such requires
Source: Ericsson. 3GPP Standardization is ongoing
LOOSE
tight
Very tight
Out of scope
from 42048