## Slide 1
Dr Kit Kilgour
5th June 2013
Motivation for HNB Emergency Warning Area Study
RP-130717

## Slide 2: HNBs provide challenges and opportunities for Cell Broadcast
Small cells allow increased granularity of warning messaging
Also a wider coverage of warning message delivery – e.g. indoors, underground, filling in coverage holes
Cell Broadcast was not built into the original HNB Iuh architecture
Only added at the end of Rel-9 as part of PWS work
Large number of cells impact size of warning messages in case of major alerts
Only current addressing option for HNB is the full SAI allocated to HNB for cell broadcast
Message from CBC to HNB-GW could require full 64k address space (> 300kByte) and significant processing and routing
Unlike LTE, 3G does not have the opportunity to group cells into Warning Areas, nor a complete RNS broadcast option (cf LTE option to broadcast to all cells under an MME)
Change of LAC causes 1-1 consequential real-time back-office link and CBC load
LAC is included as part of SAI used for Cell Broadcast
LAC change/update can be both more frequent and larger scale for HNB

## Slide 3: The proposed SID ‘HNB Emergency Warning Area’
Create a scalable Emergency Broadcast System for HNBs
Mitigate peak load on CBC and other network nodes
Look for commonalities with approach adopted for LTE to group cells
In particular the extra layer of the Emergency Warning Area
Allow operators to dimension their back-office links to Cell Location Databases and emergency warning systems appropriately
Changes of over-the-air LAC should not unduly impact these links

## Slide 4: Provisioning

## Slide 5: Operation

## Slide 6: Background

## Slide 7: Usage of LACs has changed for closed access HNBs
Historically a LAC has been broadcast over the air in order to indicate a geographical region, and has stayed relatively constant
HNB deployment has modified this paradigm
For HNBs with non-CSG UE, the OTA LAC is also used to trigger access control
SON is used for each HNB to select a LAC from a pool of LACs that is different from its neighbouring cells, causing non-CSG UE to carry out LAU and attempt
This LAC may change due to power-cycling, regional power outage, new HNBs being deployed as neighbours, location change, …
This LAC is currently an element of the SAI used for Cell Broadcast addressing
.. So every LAC change triggers back-office activity and updates to the CBC
Updates to cell location databases need to be real time rather than, say, daily and back office links and CBC have to cope with peak loading

## Slide 8: LAC usage for closed access HNB deployment
LAC usage for HNB is carried out by SON self-configuration techniques allowing HNB to select from an available pool
UEs are rejected from a HNB using a LAU Reject code
SIM only has to retain last 10 rejected LACs
Operators want to minimise unnecessary over-the-air signalling for failed accesses
It is desirable to keep the LAC pool in an area to close to 10 in size
All options have pros and cons
Single over-the-air LAC doesn’t generate LAUs
  UE in idle model will camp on cells it may not have access permissions to, rejected when requests service
  Problems in co-channel deployment or isolated cell – UE may not find (or there is no) macro to provide service
Large LAC pool may offer greater LAC stability
  But generates unwanted over-the-air signalling for failed accesses

## Slide 9
Any information provided in this document does not imply a binding commitment by ip.access. Any roadmap or forward looking statements represent reasonable estimates, based on ip.access’ current internal plans and understanding of existing circumstances (such as standards, technologies and market situation).
The information is subject to change at the sole discretion of ip.access at any time. ip.access accepts no liability for any reliance on this information unless otherwise expressly agreed in writing. The information constitutes ip.access’ confidential information