## Slide 1
3GPP TSG-RAN #62 RP-131762
Busan, Korea, 3rd– 6th December 2013
Source: China Unicom
Title: Motivation for the WI proposal: Scalable UMTS Time dilated solution
Document for: Discussion
Agenda Item: 13.1.1

## Slide 2: Motivation
The SI on Scalable UMTS FDD Bandwidth is proposed to be completed at RAN#62.
TR25.701 is presented for approval and all parts are completed.
It is proposed to start a WI focusing on the following objectives:
    Specify mechanisms that enable the UMTS Time Dilation solution
    Define Scalable UMTS configurations
    Define the necessary Access Stratum protocol changes (Layer 1/2/3)
    Mobility enhancement
    Define the RF requirements and evaluate potential core/performance requirements changes

## Slide 3: Deployment Scenarios and Use Cases
Standalone Scalable UMTS
  Band VIII: 3.6MHz GSM+ 2.4MHz S-UMTS
  Transitional period of refarming GSM system
  Deploy specific use cases such as small cell and MTC
Carrier aggregation of Scalable UMTS with UMTS
  Band VIII: 5MHz UMTS+ 1.25MHz S-UMTS
  For GSM refarming requirement and increase the feasibility of UMTS system
  Use case: hotspot capacity requirement
S-UMTS
UMTS
5 MHz
1.25 MHz
Band VIII 6MHz

## Slide 4: Outcome of the SI (1/3)
Proposed solutions during the SI
  Time Dilation: the UMTS chip rate is scaled by a factor of N which reaches a smaller bandwidth.
  Scalable UMTS by Filtering: achieves a lower bandwidth by modifying the RRC filter to match the target bandwidth and experiences larger Inter Symbol Interference than normal UMTS.
  Scalable UMTS by filtering and chip zeroing / Spreading factor dilation: zeroing all chips except every Nth chip of the 3.84Mcps UMTS signal.
Link level results
  Time Dilation:
    DL: 75% to 100% of the spectral efficiency of UMTS .
    UL: -6% to 4.36% gain of spectral efficiency of UMTS under 10% BLER after 1 transmission
  Scalable UMTS by Filtering:
    DL: spectral efficiency losses of 20% to 66% at high C/I levels and zero-to-little losses at low C/I levels compared to UMTS
    UL: a small loss was seen at low data rates and the loss increases as a function of data rate

## Slide 5: Outcome of the SI (2/3)
System level results for time dilated solution
  In bursty traffic of low load scenarios, the downlink burst rate of time-dilated UMTS N=2 is in the range 4-10% less than ½ of UMTS.
  When N=4, the burst rate is in the range 4-7% less than ¼ of that for UMTS at low loads.
  Carrier aggregation scenario:
    7.5MHz bandwidth and N=2: performance can improve by around 50% as expected for bursty traffic
    6MHz or more bandwidth and N=4: the performance gains are around 25% for bursty traffic models

## Slide 6: Outcome of the SI (3/3)
Impacts on latency for time dilated solution
  Considering 3 maximum retransmissions in the worst case , maximum HARQ RTT is increased to 72-96 msec for N=2 and 144-192 msec for N=4.
  The user plane latency on the uplink can be mitigated by utilizing the excess power available on the uplink.
  Signalling latency: the call setup delay would not increase significantly if mitigating factors were taken into account .
  Analysis of other aspects for time dilated solution
  Coverage:
    For voice service, time-dilated UMTS will have around 1dB lower coverage than normal UMTS if the same carrier power is assumed.
    For E-DCH, time-dilated UMTS provides similar coverage to normal UMTS if same PSD is assumed, and a 3 dB higher coverage when same carrier power is assumed.
  When CPC is considered, the link efficiency for time-dilated UMTS was shown to be comparable to UMTS.
  In CPC DTX/DRX, for single TTI packet sizes no increase in on-time percentage at the UE; in web browsing scenarios , an increase in the on-time percentage of around 9% on the DL and 6% on the UL.
Impacts on RAN1, 3, 4 and RAN5 specifications: have been investigated during the SI