## Slide 1: Motivation for Inter-eNB CoMP for LTE
Samsung, KT, LG Uplus, SK Telecom
RP-131923
3GPP TSG RAN Meeting #62
Busan, Korea, 3 – 6 December 2013

## Slide 2: CoMP in Rel-11
Rel-11 CoMP focused on air-interface between UE and network
  No network interface was specified (ideal/proprietary backhaul was assumed)
CoMP techniques considered in Rel-11
  Coordinated scheduling/beamforming (CS/CB)
  Dynamic point selection (DPS)
  Joint transmission (JT)
DPS
JT
CS/CB

## Slide 3: CoMP-NIB (Non-Ideal Backhaul) in Rel-12
Objective of CoMP-NIB study item:
  Evaluation of inter-eNB CoMP considering delay from non-ideal backhaul
  For coordinated scheduling and coordinate beamforming including semi-static point selection/muting
Outcome of CoMP-NIB study item
  Performance gain of Inter-eNB CoMP varies as a factor of
    deployment scenario
    backhaul delay
    coordination scheme (centralized vs distributed)
    scheduling approach
    resource utilization factor
    coordination size

## Slide 4: Performance Results (CoMP scenario 2)
In case of 5ms backhaul delay and high RU (0.5-0.8)
  For coordination size of 9, it is observed that
    5% UPT gain has a median of -3.2% and a range of -6.0% ~ 6.8%
    Mean UPT gain has a median of -4.7% and a range of -6.9% ~ 7.0%
  For coordination size of 21, it is observed that
    5% UPT gain has a median of 0.5% and a range of -23.0% ~ 24.7%
    Mean UPT gain has a median of -5.2% and a range of -12.4% ~ 13.1%
CoMP scenario 2
from TR 36.874

## Slide 5: Performance Results (SCE scenario 1)
In case of 5ms backhaul delay and high RU (0.5-0.8)
  (Sparse) For 4 small cells within one macro area, it is observed that
    5% UPT gain has a median of 11.4% and a range of -9.6% ~ 16.2%
    Mean UPT gain has a median of 6.1% and a range of -11.6% ~ 10.3%
  (Dense) For 10 small cells within one macro area, it is observed that
    5% UPT gain has a median of 16.4% and a range of 7.4% ~ 21.3%
    Mean UPT gain has a median of 1.4% and a range of -0.4% ~ 13.8%
SCE scenario 1
from TR 36.874

## Slide 6: Performance Results (SCE scenario 2a)
In case of 5ms backhaul delay and high RU (0.5-0.8)
  (Sparse) For 4 small cells within one macro area, it is observed that
    5% UPT gain has a median of 6.8% and a range of -9.1% ~ 27.0%
    Mean UPT gain has a median of 5.1% and a range of -25.2% ~ 16.4%
  (Dense) For 10 small cells within one macro area, it is observed that
    5% UPT gain has a median of 11.7% and a range of 4.0% ~ 17.4%
    Mean UPT gain has a median of 22.9% and a range of -0.5% ~ 27.0%
SCE scenario 2a
from TR 36.874

## Slide 7: Conclusions
Observation from CoMP-NIB study item evaluation results
  Centralized coordination of wireless resources, if properly done, can provide significant system performance enhancement
  X2 is designed for peer-to-peer eNB signaling, making it inappropriate for centralized coordination of large scale
Proposal
  Start RAN3 work item to specify a new interface (C1) between eNBs and a centralized coordinator
Centralized Coordinator
C1
C1

## Slide 8: ANNEX : Delay Impact of Inter-eNB CoMP with Non-Ideal Backhaul

## Slide 9: Delay Analysis on CoMP-NIB
Some companies expressed concerns that a centralized coordination of wireless resources incurs additional delay on packet delivery
Following set of slides are provided to address the above issue
  Evaluation results show that the overall delay on packet delivery is reduced, not increased

## Slide 10: Overall Delay in Packet Delivery
Overall delay in packet delivery is the sum of T_W and T_TX
  T_W : waiting time to assign available resources
    May include time duration between the point of eNB requesting resource allocation and the point of eNB being allocated resource
    May increase as the backhaul delay increases
  T_TX : transmission time for packet delivery
Concern from some companies is that due to T_W, centralized coordination might end up increasing overall delay on packet delivery
T_W
T_TX
T : Required time for packet delivery
Packet arrival
Packet completion
Initial scheduling

## Slide 11: Evaluation Result
Overall delay in packet delivery is reduced significantly even in non-ideal backhaul
  Increase of T_W much less than decrease of T_TX  Overall delay of packet delivery reduced
Scheme | Backhaul Delay | Avg T_W + T_TX | Avg T_W | Avg T_TX
Reference | 0 | 570.9 | 10.9 | 559.9
CoMP | 5 | 440.1 | 18.8 | 421.3
CoMP | 10 | 460.1 | 23.9 | 436.2
Overall packet delay reduced
[ms]

## Slide 12: Evaluation Environments
Simulation parameters
  Scenario : SCE scenario 2a (sparse)
  CoMP scheme : coordinated scheduling (CS)
    Step 1 : Coordinated scheduling is performed to decide the resource allocation for each eNB in the resource coordinator
    Step 2 : Each eNB conducts UE scheduling on the assigned resource with the latest CSI
  Reference scheme : non-CoMP
  Backhaul delay : 5ms, 10ms
  RU : high RU (60%)
  Detailed parameters : R1-135826 (SCE 2a)