## Slide 1: Way Forward on Next-step of NAICS Study Item
MediaTek, Qualcomm, Verizon, CATT, CMCC, CATR, NTT DoCoMo, Ericsson, CHTTL, Sprint, ITRI, Samsung, T-Mobile USA, ALU,
3GPP TSG RAN #62
Busan, South Korea, 3-6 December 2013
RP-132123

## Slide 2: Background
Significant progress since SI approved in RAN#59 [see TR 36.866]
  Both RAN1 and RAN4 observed that E-LMMSE-IRC/SL-IC/R-ML all showed noticeable gains over baseline MMSE-IRC receivers
  RAN1: Compared to requiring NAICS receivers to detect all interference parameters, some network signalling/coordination can be beneficial for reducing receiver complexity and/or improve performance with increased robustness
  RAN4: The next focus will be the evaluation of the performance and complexity of blind detection of interference parameters, including which parameters to be blindly estimated by the UEs and which will be network assisted
Both RAN1 (60-70% completion level) and RAN4 (70-80% completion level) have open issues with respect to the original SID scope

## Slide 3: Way Forward
RAN1 and RAN4 should have the following focus and target completion at RAN#63:
  (RAN1) Identify the interference transmission parameters for signalling and those for receiver detection, based on the following studies and the trade-offs:
    Receiver performance and complexity, with and without network assistance (RAN4)
    Feasibility of assistance signalling and system performance that takes into account corresponding signalling overhead (RAN1)
      Focus first on higher-layer based assistance signalling
    Network performance evaluation if any network coordination is assumed that introduces scheduling constraints (RAN1).