## Slide 1: Motivation of New WI Proposal on Network Assisted Interference Cancellation and Suppression for LTE
Copyright © MediaTek Inc. All rights reserved.
RP-140207
TSG-RAN Meeting # 63
Fukuoka, Japan, March 3 - 6, 2014
MediaTek Inc (Rapporteur)

## Slide 2: Background
NAICS SI started in March 2013
Original planned completion: December 2013
Extended in December 2013 to March 2014, with the reduced focus as agreed in RP-132108:
  (RAN1) Identify the interference transmission parameters for signalling and those for receiver detection, based on the following studies and the trade-offs:
    Receiver performance and complexity, with and without network assistance (RAN4)
    Feasibility of assistance signalling and system performance that takes into account corresponding signalling overhead (RAN1)
    Network performance evaluation if any network coordination is assumed that introduces scheduling constraints (RAN1).

## Slide 3: RAN1 Conclusion (1/3)
Higher-layer signaling of parameters related to interference PDSCH could be beneficial to reduce the blind detection complexity or performance degradation
  It is not precluded at yet that some of the following candidate parameters may be blindly detected
  Candidate parameters for higher-layer signaling for further study both in RAN1 and RAN4 include
    Resource allocation granularity (e.g., a group of PRB or PRB pairs)
    RA type (e.g., type 0, LVRB, Ngap used for DVRB)
    System bandwidth
    Synchronization indication (e.g., CP length)
    CSI-RS configuration
    QCL
    Cell-ID
    CRS ports
    MBSFN pattern
    ρB/ρA

## Slide 4: RAN1 Conclusion (2/3)
For the following parameters of interference PDSCH, UE blind detection is desirable to reduce scheduling restriction and signaling overhead, possibly detected from a reduced subset (e.g., RRC signaled) of all values for some parameters
  Presence or absence of interference
  TM
  For DMRS-based TMs: DMRS ports, modulation order, Virtual cell ID, nSCID, Cell ID, CRS ports, and MBSFN pattern
  For CRS-based TMs: PMI, RI, modulation order, Cell ID, CRS ports, and MBSFN pattern, ρA
  CFI (if not coordinated and required by receiver implementation)

## Slide 5: RAN1 Conclusion (3/3)
Further investigation of CSI enhancement is needed in order to help to ensure that NAICS receivers can achieve a user throughput gain
Dynamic signaling from an interference or a serving cell can be evaluated after conclusions on blind detection, conditions and assumptions including the physical channel and assumed content can be further discussed

## Slide 6: RAN4 Conclusion on Performance
E-LMMSE-IRC/SL-IC/R-ML/CWIC all achieve noticeable performance gain over Rel-11 LMMSE-IRC receiver in most scenarios , and the gains depend on the different interference profiles

## Slide 7: RAN4 Conclusion on Blind Detection
Blind detection for some parameters was found acceptable in terms of complexity and performance in some cases (e.g., under some interference conditions), but not in some other cases and further study is needed.
  For all transmission modes, at least the modulation order can be blindly detected assuming all other parameters are known.
  For CRS-based transmission modes, at least PMI rank-1 (2 CRS ports) can be blindly detected assuming all other parameters are known.
  For all transmission modes, the presence of interference PDSCH can be blindly detected assuming all other parameters are known.
  For DMRS-based TM, at least DMRS ports (with restriction to port 7/8) and modulation order can be blindly detected assuming all other parameters are known.

## Slide 8: RAN4 Working Assumptions
Working assumption: For CRS-based transmission modes, at least RI can be blindly detected assuming all other parameters are known.
Working assumption: limit the scope of Rel-12 study to total layers (serving + interfering) up to 3 and number interferer to cancel to 1

## Slide 9: Current Status
Compared with the focus in RP-132108, the following elements were completed in RAN1 and RAN4:
  RAN1 identified candidate interference parameters for higher-layer signalling and parameters that are desirable for UE blind detection in order to reduce scheduling restriction and signaling overhead, possibly detected from a reduced subset (e.g., RRC signaled) of all values for some parameters.
  RAN4 concluded that blind detection for some parameters was found acceptable in terms of complexity and performance, for example under some interference conditions or when others parameters are assumed known.
Technical issues for next-step study are captured in the SR, but companies have different views on whether the study item objective in RP-132108 is achieved or not
  i.e., remaining technical issues can be addressed in WI or SI?

## Slide 10: FFS Issues (1/2)
RAN1 has not concluded on the exact parameters or their subset restriction, after RAN1 identified the candidate interference parameters for higher-layer signalling and parameters that are desirable for UE blind detection
  The conclusions will take into account the impact of higher-layer signalling or network coordination, including signalling overhead and the impact of any scheduling restriction due to subset restriction.
  Depending on the conclusion for blind detection under higher-layer signalling, dynamic signalling from an interference or a serving cell can be evaluated.

## Slide 11: FFS Issues (2/2)
RAN 4 has not concluded the exact parameter combinations that could be detected jointly, including if under any subset restriction for any parameters, after RAN4 concluded that blind detection for some parameters was acceptable in terms of complexity and performance in some cases (e.g., under some interference conditions), but not in some other cases and further study is needed.
Further investigation of CSI enhancement is needed in RAN1 in order to help to ensure that NAICS receivers can achieve a user throughput gain.

## Slide 12: Debate on Completion level
RAN1 completion level ranges from 80-100% in company views
RAN4 completion level ranges from 80-100% in company views

## Slide 13: Motivations for WI approval
In order to realize the observed gains of identified NAICS receivers in commercial deployments as early as possible, it is proposed to start the work item phase to further agree on the exact parameters for signalling based on the candidates already identified and specify necessary signalling. After the necessary signalling is defined, the appropriate receiver performance can be specified in RAN4.
  What it also proposed is to close the SI and have one-step approval of TR36.866 version 2.0.0

## Slide 14: Proposed WI Scope (1/2)
The work item is to specify network assistance signalling for LTE downlink data channels and SL-IC and R-ML receivers under inter cell interference scenarios. In the Rel-12 scope, the advanced receiver is assumed to be capable of processing up to 3 total layers (serving + interfering) and cancelling 1 interferer.
The detailed objectives include:
  (RAN4) Identify parameter combinations that could be detected jointly, including if under any subset restriction for any parameters.
    Parameters are limited to those identified in the study item phase as desirable for blind detection, namely:
      Presence or absence of interference
      Transmission modes (TM)
      For DMRS-based TMs: DMRS ports, modulation order, Virtual cell ID, nSCID, Cell ID, CRS ports, and MBSFN pattern
      For CRS-based TMs: PMI, RI, modulation order, Cell ID, CRS ports, and MBSFN pattern, ρA
      CFI (if not coordinated and required by receiver implementation)

## Slide 15: Proposed WI Scope (2/2)
(RAN1) Agree on the parameters, including any subset restriction, for which higher-layer signalling can be used to reduce receiver blind detection complexity or performance degradation.
  Starting from the candidate parameters identified for higher-layer signalling in the study item conclusion.
  Taking into account and evaluating the impact of higher-layer signalling, including signalling overhead and the impact of any scheduling restriction due to subset restriction
(RAN1) Investigate CSI enhancements for NAICS receivers; if necessary specify the identified enhancements.
(RAN1) Depending on the conclusion for blind detection under higher-layer signalling, dynamic signalling from an interference or a serving cell can be evaluated.
(RAN2) Specify higher-layer signalling as agreed in RAN1.

## Slide 16
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com