## Slide 1: Motivation of the New SI Proposal: Study on Licensed-Assisted Access using LTE
Huawei, Ericsson, Qualcomm, HiSilicon
3GPP TSG RAN Meeting #64 RP-140786
Sofia-Antipolis, France, June 9-12, 2014
Document for: Discussion
Agenda Item: 14.1.1

## Slide 2: Motivation (1/2)
Striving to meet the market demands, there have been increasing interests from operators in deploying some complementary accesses utilizing unlicensed spectrum to meet the expected traffic growth, with maintaining the carrier user experience on quality, security, mobility, etc.
  Unlicensed Spectrum available for any interested party
Chart: 
| 2.4GHz | 5.1GHz | 5.3GHz | 5.4GHz | 5.8GHz | 5.9GHz
 | 83.5 | 200 | 120 | 200 | 125 | 75
Chart: 
| USA | CANADA | UK | Japan
2008 | 197983.6499 | 8262.7738 | 22254.5733 | 81540.0431
2009 | 309152.9541 | 15163.6852 | 43798.6349 | 170560.9227
2010 | 511338.5883 | 27151.2642 | 82032.6073 | 306961.088
2011E | 901886.8612 | 48528.3837 | 156788.9012 | 531203.1613
2012E | 1647995.4444 | 89834.8231 | 307913.76 | 943158.8662
2013E | 3058654.3011 | 169178.3093 | 597595.1627 | 1718412.2678
2014E | 5765737.0256 | 320449.0659 | 1118253.5962 | 3084485.8931
  MBB Traffic Increase, e.g. X 1000@2020
Source: Huawei Wireless 2011 Q1（Based on Informa 2010Q3)
Traffic doubled every year
MHz

## Slide 3: Motivation (2/2)
Licensed spectrum with exclusive usage is superior for telecommunication services
  Guaranteed security, coverage, mobility, QoS, …
  Spectrum resource might be limited in some area to meet MBB traffic requirement during busy hours
Using LTE for a Licensed-Assisted Access to unlicensed spectrum can only be a complement
  Some operators use WiFi offloading for capacity boosting
  LTE-based access can provide benefits, with licensed-assisted access

## Slide 4: Scenarios & Deployments
Public
Operator deployment
Indoor/Outdoor
Residence
Personal deployment
  Deployments – Non-standalone
  Scenarios – Operator-Controlled
  Unlicensed carriers are integrated into operator networks
  with Licensed-Assisted Access
Co-located
Non-co-located
+
Micro/Pico/RRH
Micro/Pico/RRH

## Slide 5: Requirements
Efficient Hotspot Traffic Offloading:
  Efficient Air-Interface: reuse LTE physical-layer design and numerology as much as possible
  Based on Carrier Aggregation Framework: Integration of unlicensed carriers into LTE licensed system
Unified Operation and Management:
  Guaranteed User Experience with uniform telecom-level QoS
  Common authority and security with transparent switch of unlicensed/licensed carrier
  Joint operation, load balancing and interference management
Co-existence: common solution to address global situation
  Coexistence of the licensed-assisted accesses among different operators that are sharing the same unlicensed band
  Coexistence with other technologies in the same band, i.e. WiFi

## Slide 6: Licensed-Assisted Access of LTE in Unlicensed Spectrum
Licensed LTE
Unlicensed Carriers
DL only
Primary
Carrier
DL-only
Secondary
Carrier
Licensed LTE
Unlicensed Carriers
TDD
Primary
Carrier
DL and UL
Secondary
Carrier
Non-Standalone: CA-based candidate solutions
Licensed-assisted access in unlicensed carriers
Unlicensed Carriers
Without Licensed LTE, unlicensed access will lose these advantages
Standalone
Controlled by Operator Network
Coverage
& Capacity Guarantee
Mobility and service continuity
QoS
Guarantee
Unified
OAM, RRM, etc.
Notes: 影子

## Slide 7: Tentative Standards Plan
Tentative standard schedule:
  Start RAN WG SI at RAN#65
  Complete solution addressing global situation in Rel-13
Before RAN WG SI, RAN could already
  Identify the most important deployment scenarios and requirements
  Summarize regional regulatory status and restrictions, and recommend high priority unlicensed bands and band combinations
  Define the scope of needed coexistence studies for integrating unlicensed spectrum operation to LTE
64
65
66 Dec’14
67
68
69
70 Dec’15
RAN WG SI
RAN WG WI