## Slide 1: User Plane Congestion management (UPCON) in Rel-13
NEC
3GPP TSG RAN#64,
Sophia Antipolis, France, June 10th – 13th 2014
RP-140847

## Slide 2: SA2 UPCON Work Item Structure
UPCON Building Blocks as per SP-140153:
BB I: UPCON-DOTCON
  RAN Downlink Traffic Differentiation (e.g. marking, priority, etc.)
  Congestion Detection (decision at SA2#103: will not be developed further)
  Congestion Reporting
  CN Congestion Mitigation mechanisms
  Dynamic Policy Control, incl. Application/RX handling
BB II: UPCON-CON (no agenda time yet)
  Content specific UP prioritization (Video)
  Application specific UP prioritization
BB III: UPCON-TRAF (no agenda time yet)
  Uplink traffic and attended/unattended traffic

## Slide 3: SA2 UPCON selected solutions
Solution# | Solution type | Solution Title | Potential Candidate (Y/N/comments)
1 | CN based | 1.5.1: GTP-U extension & 1.6.1: Policy-based congestion mitigation | N
2 |  | 1.5.2: C-Plane Signalling & 1.6.1: Policy-based congestion mitigation | N
3 |  | 1.5.3: RPPF based congestion reporting & 1.6.1: Policy-based congestion mitigation | N
4 |  | 1.5.4: Integrated On-path and Off-path & 1.6.1: Policy-based congestion mitigation | N
5 |  | 1.5.5: Off-path based & 1.6.1: Policy-based congestion mitigation | Y
6 | RAN based | 2.1: Flow priority-based traffic differentiation on the same QCI (FPI) | Y
7 |  | 2.2: Flow and bearer QoS differentiation by RAN congestion handling description (FQI) | N
8 |  | 2.3: Enhancing existing bearer concepts | N
9 |  | 2.4: Differentiation of IP flows based on flow level QCI | N
The following BB I solutions have been selected in SA2#104:
(table from TR 23.705 V0.11.0 available at ftp://ftp.3gpp.org/tsg_sa/WG2_Arch/Latest_SA2_Specs/Latest_draft_S2_Specs/23705-0b0.zip)

## Slide 4: SA2 UPCON WI status after SA2#104
Final conclusions (TR 23.705 V0.11.0):
It is concluded that the solutions 1.5.5 Off-path based and 1.6.1: Policy-based congestion mitigation are to be added into normative specifications.
Editor’s Note: Only the study of the solution 2.1: Flow priority-based traffic differentiation on the same QCI (FPI) is still ongoing for the RAN based solutions.
Discussion:
For the selected CN-based solution (off-path), there is no need for RAN standardization work, since congestion detection will be done in a new functional entity (RCAF) in CN based on OA&M data.
For the RAN-based solution, an LS will be sent in the next SA2 meeting #105 to RAN2/3, asking to evaluate the feasibility of the DL packet marking (FPI) solution.