## Slide 1
LG Electronics Inc., Pantech, Samsung, NEC, ETRI, Kyocera, Fujitsu, AsusTek
Way Forward on UL Bearer Split in Dual Connectivity
3GPP TSG RAN-64 Sophia Antipolis, France, 10 - 13 June 2014

## Slide 2: Progress on UL Bearer Split in RAN2
What is UL Bearer Split?
  UE can transmit UL PDCP data to both MeNB and SeNB.
RAN2#83bis (2013.10)
  The issue was first brought up.
  Decided to support DL bearer split, but no decision on UL bearer split.
RAN2#84 (2013.11)
  Agreed to allow UL RLC Status PDU transmission to both eNBs.
  No decision on UL PDCP data transmission
RAN2#85 (2014.02)
  Indicative voting showed equal split between support and non-support (15:15).

## Slide 3: Progress on UL Bearer Split in RAN2
E-mail discussion on UL bearer split [1] (2014.02~2014.03)
  Major issue is how to calculate PDCP data available for transmission in BSR.
    1) report the same amount of data identically to both eNBs. (3)
    2) report the data as being available for transmission towards one eNB only. (5)
    3) tailor the report based on signalled ratio. (11)
    4) report the amount of PDCP data as zero to both eNBs. (2)
    5) report the data as being available for transmission towards one eNB only until it exceeds a threshold. If the available data is above the threshold, the exceeded amount of data is reported to the other eNB. (1)
  E-mail discussion suggested to go for option 3.

## Slide 4: Progress on UL Bearer Split in RAN2
RAN2#85bis (2014.04)
  Indicative voting showed equal split between support and non-support (17:17).
  Agreed not to support UL bearer split in Rel-12 assuming that it causes less complexity and helps the progress of the WI.
RAN2#86 (2014.05)
  A document (R2-141987 [2]) was submitted with multiple co-sourcing companies to revert the decision, and go for option 1.
  No consensus to agree the proposals of this document and allow for further discussions.

## Slide 5: Difficulties in supporting UL Bearer Split
All the options supporting UL bearer split are not working perfectly.
  Option 1: Double reporting leads to over-scheduling
  Option 3: Single SDU cannot be split. Difficult to set the optimal ratio.
  Option 4: No reporting leads to under-scheduling.
  Option 5: Difficult to set the optimal threshold.
Still many issues are left in RAN2
  If the UL bearer split is supported, the BSR impacts should be discussed in RAN2 User Plane parallel session, but the UP session is already packed with remaining open issues.
    E.g. PDCP reordering, PDCP status reporting, PDCP re-establishment, PBR setting in LCP, DRX coordination, design of PHR MAC CE, Random Access, SPS support, Time Alignment, Activation/Deactivation, etc.

## Slide 6: Difficulties in supporting UL Bearer Split
RAN2 spent lots of meeting time on DC
  ... but it is questionable whether RAN2 can complete DC WI until December even without UL bearer split, considering lots of remaining open issues!

## Slide 7: Way Forward on UL Bearer Split
Proposal1: For Rel-12, stick to the current agreement that UL bearer split is not supported.
Proposal2: Support of UL bearer split is discussed again in Rel-13 with the evaluation of all possible options.

## Slide 8: References
[1] R2-141102 Uplink Bearer Split Email Discussion Summary; NSN
[2] R2-141987 Uplink Transmissions in Dual Connectivity; NSN, Broadcom, CMCC, Deutsche Telekom, KT Corporation, Mediatek, Nokia Corporation, Panasonic, Qualcomm