## Slide 1
3GPP TSG RAN#65
RP-141227: Open Items for 3GPP/WLAN Radio Interworking (Motivation for Exception Request for 3GPP/WLAN Radio Interworking RP-141226)

## Slide 2: Motivation for Exception Request for 3GPP/WLAN Radio Interworking
3GPP/WLAN Radio Interworking has made good progress, but there are still important elements that need to be properly addressed. We hope these elements will be prioritized for discussion during the next two RAN2 meetings.
  WLAN metrics;
  RAN rules interactions with WLAN channel reselection and WLAN AP reselection.

## Slide 3: WLAN Metrics
RAN2 has NOT solicited IEEE opinion regarding what WLAN metrics shall be used for WLAN network selection and traffic steering. However, IEEE proactively provided suggestions as indicated in the Reply LS to RAN2 and SA2 (R2-143022)
Understanding that the objective of the mechanism is to select the network that provides the best match to the QoS and/or throughput requirements of the system, the consideration of RSNI/RCPI is not sufficient on its own to efficiently estimate the available throughput and QoS that will be experienced in the IEEE 802.11 WLAN. Other metrics should be taken into account, especially channel bandwidth, operating band, number of spatial streams, BSS load, and WAN metrics, see also the attached Table 1. Comparing only the RSNI/RCPI, as is, to thresholds presents some risks of poor decisions. Ideally, a single parameter, such as estimated available throughput, which combines all of the above parameters, would be determined inside of the WLAN modem and then delivered to the upper layers.
Estimated available throughput has now been defined at the 802.11 SME interface as specified in IEEE 802.11-14/0792r7 [3], which has been accepted by the IEEE 802.11 Task Group mc (Maintenance and Revision). The value of this parameter is determined inside of the WLAN modem and then delivered to a requesting upper layer entity such as a 3GPP connection manager.

## Slide 4: WLAN Metrics – discussion and decision in SA2
The first LS from SA2 to RAN2 (S2-142200): " SA2 would like to inform RAN2 that SA2 agreed not to use the WLAN thresholds for Channel Utilization Level and backhaul data rate provided by the RAN as assistance parameters for traffic steering in ANDSF. ANDSF-provided thresholds for these metrics are however used in WLANSP for WLAN network selection… SA2’s understanding is that these thresholds are useful for WLAN network selection as they allow the UE to choose a less loaded WLAN AP. However, when the UE is already attached to a WLAN AP, these thresholds are not sufficient to determine if the service quality of the WLAN AP can meet or not the required service quality as indicated in the Reply LS sent by IEEE 802.11 WG to RAN2 and SA2 [S2-142033]. "

## Slide 5: WLAN Metrics: Proposal 1
RAN2 have also discussed the “estimated available throughput” metric but could not reach a conclusion because of concerns regarding the computation of this metric which is not specified.
IEEE defined the estimated available WLAN throughput metric and informed 3GPP in July 2014;
IEEE is working on defining a standard formula for computing the WLAN throughput metric during the September 2014 meeting.
Proposal 1: RAN should recommend RAN2 to consider to further discuss the WLAN metrics for 3GPP/WLAN Radio Interworking if IEEE succeeds in defining a standard formula for computing the WLAN throughput metric before the next 3GPP RAN2 meeting.

## Slide 6: RAN rules interactions with WLAN channel reselection and WLAN AP reselection.
Release 12 deployment of 3GPP/WLAN Radio Interworking solution is only available using S2 based connectivity over non-3GPP access and the cellular infrastructure and non-3GPP access may be provided using different network equipment providers and even different service operators;
IEEE also informed 3GPP that “Comparing only the RSNI/RCPI, as is, to thresholds presents some risks of poor decisions.” .
WLAN terminal device has means to mitigate poor WLAN access either by WLAN channel reselection and/or WLAN AP reselection. The process is done by the WLAN modem and it is transparent to both upper layers and 3GPP protocol stack;
RAN rules based solution may unnecessary require the UE to move its traffic from WLAN to 3GPP access when a WLAN procedure to switch to an alternative WLAN AP is in place. This creates :
  Unnecessary signaling involving core network;
  Undeterministic states due to different decisions being taken over both the 3GPP and non-3GPP Access;
  Large Power consumption on the UE due to frequent handoff process;
  Bad user experience.

## Slide 7: RAN rules interactions with WLAN channel reselection and WLAN AP reselection.
  Proposal 2: RAN should recommend RAN2 to consider the interaction between the RAN rules and WLAN channel reselection and WLAN AP reselection in the Release 12 WID.

## Slide 8: Summary
  Proposal 1: RAN should recommend RAN2 to consider to further discuss the WLAN metrics for 3GPP/WLAN Radio Interworking if IEEE succeeds in defining a standard formula for computing the WLAN throughput metric before the next 3GPP RAN2 meeting.
  Proposal 2: RAN should recommend RAN2 to consider the interaction between the RAN rules and WLAN channel reselection and WLAN AP reselection in the Release 12 WID.

## Slide 9: Thank You!