## Slide 1: Motivation for Study on Physical Layer Enhancements of Coordinated Scheduling for LTE Indoor Deployments
Ericsson
RP-141389
3GPP TSG RAN Meeting #65
Edingburgh, Scotland, Sept. 9 - 12, 2014
Document for: Discussion
Agenda Item: 14.1.1

## Slide 2: Background Indoor office
Dense user populations in indoor office environments
Large areas of open office
Wide applicability – a common scenario
Zero latency backhaul with relative ease
  Within floor of building
High capacity demand → Dense deployment
Lots of interference from many nodes!

## Slide 3: Benefits Comp for indoor office
Coordination to mitigate high interference levels
Indoor offers isolation from outdoor
  More well-defined CoMP cluster borders
Coordinated scheduling mainstream CoMP technology
Coordinated scheduling offering great performance potential
  With zero latency backhaul and with proper CSI feedback
~75%
~250%
0
2
4
6
8
10
12
14
16
0
5
10
15
20
25
30
35
Traffic per Subscriber [GB/month]
Cell-edge user throughput [Mbps]
Non-coordinated scheduling
Coordinated scheduling
+250%
+75%
Focus on improving mainstream coordinated scheduling for greatest impact!

## Slide 4: Benefits Issues with current standard for indoor comp
Current CSI feedback does not scale with CoMP cluster size
  CSI-IM overhead explodes
  CSI-IM planning a nightmare
Great potential in CSI that captures blanking of multiple nodes
  Not sufficient to only blank strongest interferer (no saturation of gains)
UE interference measurement precludes dynamic update of interference hypothesis
  Making it difficult for rank to track network load
Scalable CSI feedback without planning issue and proper interference measurement!
Chart: CoMP Gain
| Current interference measurement | Enhanced interference measurement
Interference Estimation Impact | 0.19 | 0.44
only strongest interferer blanked
no saturation of SINR gains

## Slide 5: Possible timeline for study item
RAN #65
Start of SI
RAN1 #79
RAN1 #78b
Sep
Oct
Nov
RAN #66
TR for information
Dec
Jan
RAN1 #80
Feb
Mar
RAN #67
SI finalized
Targeting complete solution for enhanced CoMP operation in Rel13!

## Slide 6: Summary
Indoor office offers great potential for gains with coordinated scheduling
CSI-IM planning nightmare and interference measurements limit performance in practice
3GPP to study scalable solutions reducing planning efforts