## Slide 1: Motivation for Study on Physical Layer Enhancements of Coordinated Scheduling for large comp cluster
Ericsson
RP-141820
3GPP TSG RAN Meeting #66
Maui, USA, December 8 - 11, 2014
Document for: Discussion
Agenda Item: nn.nn.n

## Slide 2: Background 1 Indoor office
Dense user populations in indoor office environments
Large areas of open office
Wide applicability – a common scenario
Zero latency backhaul with relative ease
  Within floor of building
High capacity demand → Dense deployment
Lots of interference from many nodes!

## Slide 3: Background 2 Large outdoor
Campus, stadium, race tracks etc.
Dense user populations in outdoor environments
Zero latency backhaul with relative ease
High capacity demand → Dense deployment
Potential for MU-MIMO scheduling
Lots of interference from many nodes!

## Slide 4: Benefits Comp for indoor office
Coordination to mitigate high interference levels
Indoor offers isolation from outdoor
  More well-defined CoMP cluster borders
Coordinated scheduling mainstream CoMP technology
Coordinated scheduling offering great performance potential
  With zero latency backhaul and with proper CSI feedback
~75%
~250%
0
2
4
6
8
10
12
14
16
0
5
10
15
20
25
30
35
Traffic per Subscriber [GB/month]
Cell-edge user throughput [Mbps]
Non-coordinated scheduling
Coordinated scheduling
+250%
+75%
Focus on improving mainstream coordinated scheduling for greatest impact!

## Slide 5: Benefits Issues with current standard for indoor comp and other large comp cluster scenarios
Current CSI feedback does not scale with CoMP cluster size
  CSI-IM overhead explodes
  CSI-IM planning a nightmare
Great potential in CSI that captures blanking of multiple nodes
  Not sufficient to only blank strongest interferer (no saturation of gains)
UE interference measurement precludes dynamic update of interference hypothesis
  Making it difficult for rank to track network load
Scalable CSI feedback without planning issue and proper interference measurement!
Chart: CoMP Gain
| Current interference measurement | Enhanced interference measurement
Interference Estimation Impact | 0.19 | 0.44
only strongest interferer blanked
no saturation of SINR gains

## Slide 6: Possible timeline for study item
RAN #66
Start of SI
RAN1 #80
Dec
Jan
Feb
RAN #67
TR for information
Mar
Apr
RAN1 #81
May
Jun
RAN #68
SI finalized
Targeting complete solution for enhanced CoMP operation in Rel13!
RAN1 #80bis

## Slide 7: Summary
Indoor office offers great potential for gains with coordinated scheduling
  Outdoor scenarios with high line of sight probability and high load are similar and offer great potential gain as well
  These new scenarios may benefit from MU-MIMO and this should be evaluated as well
CSI-IM planning for large* CoMP clusters is a nightmare and interference measurements limit performance in practice
CSI-IM overhead explodes for large CoMP clusters
Study CSI enhancements for large CoMP clusters that resolve the identified problems
  Solutions should be scalable in increasing cluster size to reduce operator planning efforts while minimizing overhead
*larger than three cells