## Slide 1: Enhanced LTE D2D Proximity Services: Release 13 D2D WI
3GPP TSG RAN #66
Maui, USA, 8-11 December 2014, Maui, USA
Agenda Item 14.1.1
RP-141905

## Slide 2: Background
Rel-12 RAN WI on Proximity Services opened in March 2014 covering
    D2D discovery for in network
    D2D broadcast communication for both in network and out of network coverage
    RAN1 & RAN2 parts should close in December 2014, extension for RAN4
Rel-13 SA2 WI on Enhanced Proximity Services opened in June 2014
    ProSe Direct Discovery for Public Safety use;
    Support for model B ProSe Direct Discovery for all use cases (i.e. open and restricted);
    Status determination and reporting, including location status, Presence status, Group status
    ProSe UE-UE relays and UE-Network relays for Public Safety use;
    ProSe Direct Communication one-to-one for Public Safety use;
    Requirements for service continuity and QoS/priority/pre-emption of ProSe Direct Communication
    Proximity estimation e.g. how near or how far a discovered UE is from the discovering UE.
Rel-13 SA1 WI on Enhanced Proximity Services completed in Aug 2014

## Slide 3: Proposed RAN Work Item
Complete remaining aspects of direct communication that were not completed in Rel-12
  Some enhancements to direct discovery
  Enhancements to support discovery and communication in presence of multi-carrier and inter-PLMN
Scope of proposed RAN work item
  LTE direct communication enhancements within and outside network coverage => for PS
  LTE direct discovery enhancements within and outside network coverage => for PS and commercial
  Enhance multiple carrier and PLMN support within network coverage => for PS and commercial
Planned approval in RAN #66
LTE Device to Device Enhanced Proximity Services

## Slide 4: Direct Communication
Unicast & groupcast enhancements
NW to UE relay, UE to UE relay
Service continuity, QoS,
Power efficiency, High data rate enhancements
Support for ProSe related MCPTT requirements
Continue work on items remaining from the original Rel-12 SID
Service Continuity
Groupcast
Unicast
NW to UE Relay
UE to UE Relay

## Slide 5: Direct Discovery, Multi-carrier & Inter-PLMN Support
Direct discovery:
  Support for Type 1 discovery out of coverage/partial coverage
  Model B – request/response discovery
    From SA2: support for model B ProSe Direct Discovery for all use cases (i.e. open and restricted);
Multiple carrier and PLMN support
  D2D transmissions in non-serving carrier and/or secondary cell for both communication and discovery
    Otherwise D2D devices may become concentrated on a single carrier
  Further optimize inter-PLMN and inter-frequency discovery
    UEs learn about inter-frequency/PLMN resource pools from serving cell
Enhancements to discovery, multi-carrier, inter-PLMN support
Carrier 1
Carrier 2
WAN
D2D

## Slide 6: Proposed RAN Work Item
Summary
D2D Discovery enhancements within network coverage Model B, Multiple carrier & PLMN | D2D Communication enhancements within network coverage for public safety only Unicast, Groupcast, Multiple carrier & PLMN
D2D Discovery outside network coverage for public safety only Type 1 for partial and outside network | D2D Communication enhancements outside network coverage for public safety only Unicast, Groupcast, Relays, Service Continuity

## Slide 8: Annex I: Objectives of SA1 WI eProSe (Rel-13)
To support stage 2/3 development during Release 13.
To support end-of-release 12 maintenance to review and ensure that Release 13 TS 22.278 and TS 22.115 contain all agreed ProSe Stage 1 requirements. These service requirements are to be copied from Release 12 TS 22.278 and TS 22.115 prior to removal of unfulfilled service requirements from Release 12 as per process for handling WIDs across releases.
The topics likely to be addressed in this process are:
  ProSe E-UTRA Communication between two ProSe-enabled UEs
  Restricted discovery
  Public safety out of coverage discovery
  UE-to-Network & UE-to-UE Relays
  Requesting Discovery Range Class
  Service continuity
  Moving of a user traffic session path
  WLAN QoS consideration
  Some WLAN roaming requirements
  Some third-party application interaction requirements
From SP-140386

## Slide 9: Annex II: Objectives of SA2 WI eProSe-ext (Rel-13)
As part of the TR phase
  Study architecture enhancements in order to support:
    Restricted ProSe Direct Discovery for non-Public Safety use;
    ProSe Direct Discovery for Public Safety use;
    Support for model B ProSe Direct Discovery for all use cases (i.e. open and restricted);
    Enhancements to the procedures for Open ProSe Direct Discovery such as management of ProSe Application IDs and metadata at the ProSe Function from application server over PC2 and revocation of ProSe App. Code from the ProSe Function. Any other Enhancements to the procedures for Open ProSe Direct Discovery, if need is identified in the scope of this work item;
    Status determination and reporting, including location status, Presence status, Group status, and UE Network Coverage status in ProSe for Public Safety use, if it is identified to be exchanged (as part of PC5 information exchanges) in scope of 3GPP standardization for Public Safety use. However, if it is identified that it is preferable that some of this status information is exchanged only as application layer signalling then this will not be in the scope of this WID.
    ProSe UE-Network relays for Public Safety use;
    ProSe UE-UE relays for Public Safety use;
    ProSe Direct Communication one-to-one for Public Safety use;
    Requirements for service continuity and QoS/priority/pre-emption of ProSe Direct Communication sessions as defined in TS 22.278 for the aforementioned communication scenarios.
    Study architecture enhancements in order to support proximity estimation e.g. how near or how far a discovered UE is from the discovering UE. Based on that additional ProSe discovery range classes could be introduced, if deemed necessary.
Specify selected solutions in relevant specifications
From SP-140385