## Slide 1
NTT DOCOMO, INC.
Motivation for new WI proposal:
Dedicated Core Networks (DECOR)
3GPP TSG RAN-68 Malmo, Sweden, 15 - 18 June 2015

## Slide 2: Overview on Dedicated Core Networks (DÉCOR) functionality (1/2)
The main motivation for Dedicated Core Networks (DECOR) functionality is the necessity to accommodate (but not restrictive to) M2M devices or devices with specific subscriptions in separate CN node different from CN node for normal services;
  To allow deployment of dedicated CN node tailored according to the need of M2M services, e.g., only subset of legacy functions or with a specific functionality.
  Without any UE impact, i.e., applicable for both legacy and new releases UE.
Notes: 2

## Slide 3: Overview on Dedicated Core Networks (DÉCOR) functionality (2/2)
The main functions are the following:
  During the initial access (Attach, TAU), the first/default MME receiving the initial access procedure decides to reroute this procedure to a Dedicated MME.
    Based on a new subscription based identitication (i.e., UE Usage Type)
  The eNB receiving the reroute signalling from MME, sends the initial access signaling towards the relevant dedicated MME.
  The dedicated MME finalizes the initial access (assigning MMEGI), such that from the subsequent access (connection establishment) the dedicated MME can be selected according to the legacy mechanism.
Legacy /Default CN
Dedicated (MTC) CN
smartphones
MTC devices/subscription
Rerouting
procedure

## Slide 4: Related work in SA2
SA2 indicate in their LS (S2-151997/RP-150569) that they have finalized their work.
Related agreed TR/CRs in SA2 are the following :
  TR 23.707, “Architecture Enhancements for Dedicated Core Networks”, Stage 2 (Release 13)
  S2-152107, “Introduce the Dedicated Core Network (DECOR) feature”, CR to 23.401, NTT DOCOMO, INC., et al.
  S2-151818, “Introduce the Dedicated Core Network (DECOR) feature”, CR to 23.060, NTT DOCOMO, INC., et al.
  S2-152108, “Adding support for load re-balancing within DCN”, CR to 23.401, Ericsson, et al.
  S2-151820, “Load rebalancing for SGSNs with Dedicated Core Networks”, CR to 23.236, NTT DOCOMO, INC., et al.
  S2-151322, “Update of MME load balancing for Dedicated Core Networks”, CR to 23.236, Huawei, et al.
Notes: 4

## Slide 5: RAN3 specifications impact
The following RAN functionalites are foreseen to be impacted:
  eNB NAS Node Selection Function
  S1AP/RANAP signaling to support MME rerouting function
(Possible) Impacted RAN3 specifications are as follows:
  36.300, Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Overall description; Stage 2
  36.401, Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Architecture description
  36.413, Evolved Universal Terrestrial Radio Access Network (E-UTRAN); S1 Application Protocol (S1AP)
  25.413, UTRAN Iu interface Radio Access Network Application Part (RANAP) signalling
Work item proposal for RAN3 is proposed in RP-150826

## Slide 6: References
[1] S2-151791, “Updated WID: Dedicated Core Networks {Decor}”, NTT DOCOMO, INC.
[2] S2-151997, “Request for specification of Dedicated Core Network (DECOR) feature”, LS from SA2, to: RAN3, CT4, cc: RAN, Contact person: NTT DOCOMO, INC.
[3] TR 23.707, “Architecture Enhancements for Dedicated Core Networks”, Stage 2 (Release 13)
[4] S2-152107, “Introduce the Dedicated Core Network (DECOR) feature”, CR to 23.401, NTT DOCOMO, INC., et al.
[5] S2-151818, “Introduce the Dedicated Core Network (DECOR) feature”, CR to 23.060, NTT DOCOMO, INC., et al.
[6] S2-152108, “Adding support for load re-balancing within DCN”, CR to 23.401, Ericsson, et al.
[7] S2-151820, “Load rebalancing for SGSNs with Dedicated Core Networks”, CR to 23.236, NTT DOCOMO, INC., et al.
[8] S2-151322, “Update of MME load balancing for Dedicated Core Networks”, CR to 23.236, Huawei, et al.
Notes: 6