## Slide 1
LG Electronics, Huawei, HiSilicon, CATT
Motivation for WI on
" Support for V2V services
based on LTE sidelink"
3GPP TSG RAN WG Meeting #70 RP-151942 Sitges, Spain, December 7 – 10, 2015
Agenda item: 14.1.1
Document for: Discussion

## Slide 2: Current status of LTE V2X in 3GPP
Study item on LTE-based V2X was approved in RAN#68 [1].
  The highest priority was given to PC5-based V2V until RAN#70.
  The motivation was to start a PC5-based V2V WI in December 2015 as proposed in [2].
Progress in SA WGs is on track.
  SA1 has entered the WI phase [3].
  SA2 and SA3 agreed SI in [4] and [5].
RAN1 completed the part of PC5-based V2V, i.e., the following objective in [1]:
  For support of PC5 transport for V2V services (to be completed by RAN#70 – December 2015), at least including:
    Identify necessary enhancements (e.g. of potential enhancements: mitigate impact of half duplex constraint, reduce resource collision, enhance pool structure, enhance resource patterns, SA information transmitted in same subframe as the associated data) to the resource allocation mechanism to meet identified requirements for robustness, latency, overhead and capacity [RAN1]
    Identify any necessary PC5 enhancements for high Doppler case (e.g. up to 280 km/h up to 6 GHz) such as enhanced DMRS, and also synchronization based on GNSS at least for out of coverage operation.[RAN1]

## Slide 3: Outcome of study on PC5-based V2V
TR 36.885 contains the following as the outcome of study on PC5-based V2V [6]:
  Operation scenarios and RAN aspects for consideration
  Necessary enhancements to resource allocation, physical layer structure, and synchronization of LTE sidelink
  Evaluation results and observations
  Conclusion: “It is feasible to support V2V services based on LTE PC5 interface with necessary enhancements. As identified, it is recommended to enhance at least LTE sidelink resource allocation, physical layer structure, and synchronization.”
RAN WGs are ready for WI on PC5-based V2V.
  Early completion of the corresponding specifications will enable fast preparation for device implementation and network deployment.

## Slide 4: Objective of the proposed WI
A WI is proposed with the following objectives [7]:
  Core part
    To specify enhancement to sidelink physical layer structure necessary for V2V services [RAN1]
    To specify enhancement to sidelink synchronization procedure necessary for V2V services [RAN1, RAN2]
    To specify necessary sidelink resource allocation enhancement option(s) for V2V services [RAN1, RAN2]
    To specify necessary radio protocols and RRC signaling [RAN2]
    To specify UE Tx and Rx RF requirement covering operations at up to 6 GHz carrier [RAN4]
    To specify RRM core requirement [RAN4]
  Performance part
    To specify demodulation requirements and RRM performance for the UE [RAN4]

## Slide 5: Proposed timeframe
The proposed timeframe is as follows:
  The outcome of the proposed WI can provide the basis for other V2X services, especially V2I/N and V2P services based on PC5 interface.

## Slide 6: References
[1] RP-151109, “New SI proposal: Feasibility Study on LTE-based V2X Services,” LG Electronics, CATT, Vodafone, Huawei.
[2] RP-151082, “Project management of V2X in TSG RAN,” Vodafone, LGE, Huawei, Qualcomm, Ericsson.
[3] SP-150573, “New WID on LTE support for V2X services (V2XLTE),” TSG SA WG1.
[4] S2-153532, “New SID on architecture enhancements for LTE support of V2X services,” LG Electronics.
[5] S3-152465, “New SID on architecture enhancements for LTE support of V2X services,” Huawei, LG Electronics.
[6] R1-157850, “3GPP TR 36.885 v.0.4.0 Study on LTE-based V2X Services,” LG Electronics.
[7] RP-151943, “New WI proposal: Support for V2V services based on LTE sidelink,” LG Electronics, Huawei, HiSilicon, CATT.