## Slide 1: Motivation for Work Item on UL 256QAM for LTE
Ericsson
RAN #71, Göteborg, Sweden, Mar. 7-10 2016
AI 10.1.1
RP-160196

## Slide 2: Demand in higher data rate
Higher spectral efficiency is one of multiple ways that are needed to meet the increased data rate demand
Ericsson mobility report

## Slide 3: Use Cases
Small Cells deployments
In both licensed and unlicensed spectrum
Many receive antennas at eNB
Multiple use cases for 256QAM in UL

## Slide 4: Evaluation results
Indoor small cell deployment
  1 Tx and 2 Rx
  LAA-LAA coexistence
    50/50 UL/DL traffic
  Mean user throughput
  Without EVM impairment
Significant performance gains by introducing 256QAM in UL
Mbps
Chart: 
| low load | medium load | high load
64QAM | 43 | 12 | 6
256QAM | 60 | 31 | 20

## Slide 5: Proposal
Introduce 256QAM support in UL for LTE to enable
  Significant increase in data rates in small cell deployments
  Leverage fully the benefits of many receiver chains in eNB

## Slide 7: Appendix: Work Plan
2016 Q2
  RAN1
    Define a framework for how to introduce 256QAM in the UL
  RAN4
    Specify EVM, MPR and A-MPR requirements
2016 Q3
  RAN1
    Conclude on MCS table design and complete PHY design
    Define potential new UE categories
  RAN2
    Define RRC signaling
    Define potential new UE categories
  RAN4
    Specify demodulation performance requirements if needed