## Slide 1: Motivation for New SI Enhancements of relayed COnnection via WLAN and LTE Sidelink (ECO)

## Slide 2: Why is a wearable device special?
Smart watches should support various services including voice/streaming with full mobility, almost like smart phones.
Customers expect much longer battery lifetime than smart phones, possibly almost like legacy watches.
Rel-12 PSM and Rel-13 eDRX are generally good for UE power saving. However, those features cannot fully support real-time services such as voice call and streaming service.
 | Smart Phone | Smart Watch | Smart Meter
Mobility | Full support | Full support | Limited support
Data Rate | High | medium | Very low
Delay | Sensitive service support | Sensitive service support | Insensitive service only
Battery lifetime | Relatively short (e.g. one or two days) | As long as possible | Extremely long

## Slide 3: Wearable and secondary UE
Customers will typically wear smart watches as their secondary devices while holding smart phones as their primary devices.
A smart watch including USIM can stand alone from time to time e.g. while a user is doing outdoor activity.
“A wearable UE can leverage the master phone in proximity to enhance connectivity with power efficiency.”
We belong to the same user.
In proximity
Standalone
device
Secondary
device
Not in proximity

## Slide 4: Key Study Areas (1/2)
The study on support of UE to Network relay via WLAN
  WLAN is commercially used as direct communication between smart phones and wearable devices.
  3GPP has already worked on “LTE/WLAN interworking and aggregation” which could be utilized to allow E-UTRAN to control UE to Network relay via WLAN.
WLAN
or
3GPP sidelink
NW
Relay
UE
Remote
UE
UE to NW relay
via WLAN

## Slide 5: Key Study Areas (2/2)
Service continuity in switching between Uu connection and relayed connection via LTE Sidelink / WLAN
  Short interruption in switching between Uu connection and relayed connection e.g. for real time traffic.
Mobility of UEs in the relayed connection
  Support the case where both a remote UE and a relay UE are moving together while maintaining the relayed connection
NW
Relay
UE
Remote
UE
UE to NW relay
via WLAN
Service continuity
under NW control
NW
Connection
on Uu
WLAN
or
3GPP sidelink

## Slide 6: Proposed Study Plan
The study is led by RAN2. (No RAN1 TU)
The study is scheduled to complete by September 2016.
The follow-up work is proposed to complete in Rel-14.