## Slide 1: Motivation and proposal for defining Network energy efficiency KPI and evaluation in TR38.913
Orange, KPN, Telecom Italia, Telefonica, Deutsche Telekom,Telia Sonera, Huawei, ZTE
3GPP TSG RAN#71 Meeting
Goteborg, Sweden, March 7 – 10th, 2016
RP-160373

## Slide 2: Overview regarding Wireless networks energy consumption
80% of the consumption of WN is dominated by RAN
the power consumption of the RAN is dominated by the power amplifier (for Macro BS)
Telecom part (PA+BBU+radio FE) = 80%

## Slide 3
EE Requirement from the NGMN 5G White paper
“Energy efficiency is defined as the number of bits that can be transmitted per Joule of energy, where the energy is computed over the whole network, including potentially legacy cellular technologies, Radio access and Core networks, and data centres.
5G should support a 1,000 times traffic increase in the next 10 years timeframe, with an energy consumption by the whole network of only half that typically consumed by today’s networks. This leads to the requirement of an energy efficiency increase of x2000 in the next 10 years timeframe.
Every effort should be made to obtain the energy gain without degrading the performance, but the technology should allow native flexibility for the operator to configure trade-off between energy efficiency versus performance where justified.”

## Slide 4: Evaluation method Proposal 1: capture this quantitative KPI definition in TR38.913
Traffic/s served by a base station : NGMN has already defined traffic demand targets for all scenarios
power consumed by a base station to transmit : single model for all scenario
Weight for mobile traffic load level : at least 3 load levels should be considered
Network EE = Weighted sum of Scenarios-EE (DU, U, SU, Ru)
Network
Scenario-EE = weighted sum of served traffic per second over power consumption
Chart: Example sites distribution
| Dense Urban | Urban | Sub-Urban | Rural
 | 2540.3412 | 5715.7677 | 6351.2256 | 8807.0328
PS: The weights of every scenario can be decided during the technology study phase

## Slide 5: Power consumption models
starting from a standard macro or micro base station including BBU, RRH and site support system (cooling)
Model given by IMEC (http://www2.imec.be/be_en/research/wireless-communication/power-model-html.html)
2014 : reference point
2020 - Massive MIMO
Site | Sleep mode (W) Psleep | No load (W) P0 | Full load (W) Pmax | Radiated (W)
Macro site 3 BS LTE 2x2 - 10 MHz BW - 2x46dBm (with 3 dB feeder loss) - FDD | TBD | 192 | 836 | 2x20
Small cell site 1 BS LTE 2x2 - 10 MHz BW - 2x27 dBm (RRH) - FDD | TBD | 4 | 7,3 | 2x0,5
IMEC will allow free access to power models
Site | Sleep mode (W) | No load (W) | Full load (W) | Radiated (W)
Macro site 1 sector BS TDD LTE - 10 MHz BW 128 radiating element per antenna 15 dBm output power per element | 12,2 | 13,1 | 16,4 | 4
load
Consumption
sleep mode

## Slide 6: Why we are confident a high improvement in terms of EE can be achieved?
Yes it possible to reduce the energy consumption while increasing the served traffic
Basically, the NGMN challenge could be decomposed in two parts (example) :
        X1000 the traffic demand
        /2 the energy consumption
Earth Project (2013) has obtained 50% improvement of energy consumption for 4G
GreenTouch (2015) has shown that we can reduced energy consumption by 90% while increasing the traffic by 100
More generally, there different levers for reducing energy consumption of mobile networks
        hardware (GaN substrate, Envelope tracking, electronic improvement..)
        Software (sleep modes, Green SON….)
        Architecture (NGPoP, small cells deployment, Multi-RAT managemnt)

## Slide 7: Actual sleep modes provides -10% reduction of energy consumption We need to implement efficient sleep-modes targeting -90% at zero load ! …. and we have first ideas on how to do that
The main problem was the cyclic and permanent transmission of reference signals : only micro-sleep-mode is possible
5G air-interface should integrate longer silent periods
SM 1
SM 2
SM 3
SM 4
10%
50%
70%
90%

## Slide 8
Proposal
Complete the EE KPI generic definition in TR 38.913 («7.19 Network energy efficiency) by adding the definition of an EE quantitative KPI as proposed in slide 4
We can at this stage leave the KPI target as [TBD] allowing for more NGMN discussions to fix a target that reflects what can be studied and evaluated under 3GPP RAN
Agree on the following principles and reflect them in TR38.913:
        Energy efficiency should be evaluated at least by means of system level simulations and at least in 2 deployment scenarios: one coverage limited environment (ex : Rural) AND one capacity limited environment (ex : Urban).
        Evaluation should not be for peak hour but based on a 24 hour daily traffic profile.
        The detailed evaluation methodology should be developed within 3GPP RAN Technology Study.
Note regarding the evaluation methodology: the base station load levels for each considered evaluation scenario could be recorded during simulations to be translated into energy consumption by means of a base station power model. Other methodology could also be studied.
Possible reference ETSI ES 202 706 “Environmental Engineering (EE); Measurement method for power consumption and energy efficiency of wireless access network equipment
Possible base station power model: GreenTouch
Proposals for the 24 hour daily traffic profiles could be provided by operators.