## Slide 1: Motivation for enhanced NB-IoT Work Item in Release-14
Source: Vodafone Group
Agenda Item: 10.1.1
3GPP TSG RAN#71 RP-160396
Gothenburg, Sweden, 7th – 10th March 2016

## Slide 2: Motivation
Rel-13 NB-IoT introduced a new radio access system for ultra-low complexity to meet the stringent IoT requirements.
Further enhancements are proposed for Rel-14. These are:
  Positioning / Location Services: Identifying the location of the end NB-IoT device is important for both business and consumer use cases. Enabling this when the device is indoor is particularly important, whilst maintaining low device complexity.
  Multicast /broadcast services: Support to download software/firmware to many devices efficiently and simultaneously, applicability of e.g. SC-PTM.
  Support of TDD: In order to develop the IoT ecosystem, a selected TDD configurations could be supported.
  Other optimisations: Further optimisations that were not agreed as part of Rel-13 but were generally identified to be useful.
    Further improvements in physical layer to lower device power consumption, lower complexity and to enable higher spectrum efficiency.
    Further improvement to higher layer protocols operation of NB-IoT

## Slide 3: Objectives
Positioning / Location Services: Support functionality such that a NB-IoT device can be located to an accuracy of less then 50 metres within a time of [TBD] seconds.
  The trade-off between location accuracy and complexity needs to be considered.
  Such positioning functionality should be applicable for all three coverage classes.
  The scenarios shall include both availability and non-availability of GNSS in NB-IOT devices
  Locating the UE when it is in extreme coverage and especially “deep-indoor” is important
Support multicast/broadcast functionality for NB-IoT devices at least based on enhancements to SC-PTM.
Support TDD operation (at least selected configurations) and identify a small number of unpaired frequency bands for corresponding support.
Other optimisations that were not agreed as part of Rel-13 but were generally identified to be useful.
  Further improvements in physical layer to lower device power consumption, lower complexity and to enable higher spectrum efficiency.
  Further improvement to higher layer protocols operation of NB-IoT, including interworking between NB-IOT and Non NB-IOT carrier. In general, the solution should address the Non-NB-UEs.

## Slide 4: Thank you