## Slide 1
3GPP TSG-RAN Meeting #71
Göteborg, Sweden, March 7 - 10, 2016
KT Corporation
Introducing new CA band combination in basket Rel 14 CA WIs
RP-160406

## Slide 2: LTE service in KT network
In Korea, KT has provided 3DL carrier aggregation service since Jan 2015 using 40MHz spectrum in most of dense urban area
There has been dramatic traffic increase in the LTE commercial market recently and eventually we observe some capacity warning sign in some of dense urban area
  PRB usage of certain region always exceeds 60% in busy hour.
  User experience data rate is getting decreased
  Even thought KT provides free-WiFi service in this area, customers prefer to use LTE instead of WiFi

## Slide 3: Spectrum Availability & Deploy Plan
There will be spectrum auction on MARCH 2016 in Korea. Candidate spectrums are B1, B3, B7, B28
  KT might have chance to have additional spectrum among four spectrums to solve capacity warning comes from market
  In order to satisfy use experience, KT is willing to deploy additional network right after we get the spectrum
  We are plan to launch commercial service before September 2015.
  Status of Standard that KT is interested in
    B1 related high order CA WIs are already completed
    B7 related high order CA WIs are already completed
    B28 related high order CA WIs lead by “S” operator are on going
    There is no B3 related high order CA WIs that KT needs urgently

## Slide 4: Reason of submitting proposal to RAN directly
In RAN4, following gerneral ruls was agreed
KT unfortunaltely missed ”one week” deadline
RAN4 allowed that proponents can bring their proposal in RAN meeting as discussion. If RAN approves it, corresponding combo can be included in basket WI by updating basket WID in the same plenary
Proponents on a particular CA configuration need to contact the rapporteur if they want to add their CA configuration to corresponding basket WI before minimum of one week prior to the submission deadline. Note that in order for the contact persons and the rapporteurs to share a common understanding about the request on proposed CA configurations, it would take some time. The information needs to be shared on a new reflector called “3GPP_TSG_RAN_WG4_CA@list.etsi.org”. Delegates are reminded that timely reflecting the requests for each CA configuration in advance of TSG/WG meetings is important to allow for full and fair consideration of such matters and to avoid causing troubles in RAN Plenary project management perspective

## Slide 5: Request to RAN
In order to satisfy all our valuable customer service requests, KT would like to deploy additional network right after we get the spectrum
KT requests RAN to include below two CA combinations in Rel 14 basket WIs from MARCH 2016
  B1A+B3C+B8A 4DL/1UL CA
  B3C+B8A 3DL/1UL CA
  Detailed information for WID are provided in page 6 and 7 respectively

## Slide 6: Proposed 4DL CA combination (Detailed information for WID)
CA combination | REL-indep. From | contact name, company | contact email | other supporting companies (min. 3) | status | supported next level fallback modes (in DL and UL)
CA_4DL_1A-3C-8A_1UL_BCS0 | Rel-10 | Hisashi Onozawa, Nokia Networks | hisashi.onozawa@nokia.com | KT, Ericsson-LG Samsung | New | CA_3DL_1A-3A-8A_1UL_BCS0 CA_3DL_1A-3C_1UL_BCS0
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
CA_1A-3C-8A |  | 1 |  |  | Yes | Yes | Yes | Yes | 70 | 0
 |  | 3 | See CA_3C Bandwidth combination set 0 in Table 5.6A.1-1 of TS 36.101 |  |  |  |  |  |  | 
 |  | 8 |  | yes | Yes | Yes |  |  |  | 
Table 5.6A.1-1: E-UTRA CA configurations and bandwidth combination sets defined for intra-band contiguous CA
 | E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  | 
E-UTRA CA configuration | Uplink CA configurations (NOTE 3) | Component carriers in order of increasing carrier frequency |  |  |  | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
 |  | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] |  | 
CA_3C | CA_3C | 5, 10, 15 | 20 |  |  | 40 | 0
 |  | 20 | 5, 10, 15, 20 |  |  |  | 

## Slide 7: Proposed 3DL CA combination (Detailed information for WID)
CA combination | REL-indep. From | contact name, company | contact email | other supporting companies (min. 3) | status | supported next level fallback modes (in DL and UL)
CA_3DL_3C-8A_1UL_BCS0 | Rel-10 | Hisashi Onozawa, Nokia Networks | hisashi.onozawa@nokia.com | KT, Ericsson-LG Samsung | New | CA_2DL_3A-8A_1UL_BCS2 CA_2DL_3C_1UL_BCS0
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  |  |  |  |  | 
E-UTRA CA Configuration | Uplink CA configurations | E-UTRA Bands | 1.4 MHz | 3 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
CA_3C-8A |  | 3 | See CA_3C Bandwidth combination set 0 in Table 5.6A.1-1 of TS 36.101 |  |  |  |  |  | 50 | 0
 |  | 8 |  | yes | Yes | Yes |  |  |  | 
Table 5.6A.1-1: E-UTRA CA configurations and bandwidth combination sets defined for intra-band contiguous CA
 | E-UTRA CA configuration / Bandwidth combination set |  |  |  |  |  | 
E-UTRA CA configuration | Uplink CA configurations (NOTE 3) | Component carriers in order of increasing carrier frequency |  |  |  | Maximum aggregated bandwidth [MHz] | Bandwidth combination set
 |  | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] | Channel bandwidths for carrier [MHz] |  | 
CA_3C | CA_3C | 5, 10, 15 | 20 |  |  | 40 | 0
 |  | 20 | 5, 10, 15, 20 |  |  |  |