## Slide 1: Motivation of WI proposal for Improved eMTC and NB-IOT Positioning in LTE
Ericsson
RP-160198
3GPP TSG RAN Meeting #71
Göteborg, Sweden, 7th – 10th March, 2016
Agenda item 10.1.1

## Slide 2: Justification
Rel-13 introduces two classes of low-cost MTC devices with enhanced coverage and low power consumption:
  eMTC devices with a UE bandwidth of 6 PRBs (1.08 MHz)
  NB-IOT devices with a UE bandwidth of 1 PRB (180 kHz)
As positioning is important in many MTC applications, some improvements of the positioning accuracy may also be motivated.

## Slide 3: Rel-13 status for eMTC UEs
RAN1/RAN2/RAN3
  Existing PRS is receivable by eMTC UEs
  Existing LPP and LPPa protocols are applicable to eMTC UEs
RAN4 requirements completed only for
  E-CID RSRP requirements in CE mode A and CE mode B

## Slide 4: Objective for eMTC UEs
Existing positioning methods
  Complete RAN4 requirements (core part and performance part):
    OTDOA: RSTD (UE measurement)
    E-CID:
      RSRQ (UE measurement)
      UE Rx – Tx time difference (UE measurement)
      Timing Advance Type 1 (E-UTRAN measurement)
      Timing Advance Type 2 (E-UTRAN measurement)
New signal and/or configuration
  OTDOA: RAN1 to define new PRS configurations to improve positioning accuracy of eMTC UE
  UL signal based positioning: RAN1 to define new UL signal configuration to improve positioning accuracy of eMTC UE
  RAN1/RAN4 requirements for the new DL and UL measurements

## Slide 5: Rel-13 status for NB-IoT UEs
RAN1
  Existing LTE PRS is not receivable by NB-IoT UEs
    Not receivable even for UEs in in-band deployment mode
RAN2 agreement
  Positioning can be supported by eNB measurements
  RAN2 assume that some variant of CID could be supported in Rel-13
  RAN2 assume there is no UE support for RAT-measurements in Rel-13
  No Rel-13 work for this is expected in RAN2

## Slide 6: Objective for NB-IoT UEs
OTDOA
  Define PRS and related requirements for NB-IoT of all deployment modes
    In-band
    Guard band
    Standalone
E-CID
  RAN1/RAN4 requirements (core part and performance part)
    RSRP (UE measurement)
    RSRQ (UE measurement)
    UE Rx – Tx time difference (UE measurement)
    Timing Advance Type 1 (E-UTRAN measurement)
    Timing Advance Type 2 (E-UTRAN measurement)
UL signal based positioning
  Define UL signal transmission for NB-IoT UEs
    Multi-tone and single-tone