## Slide 1: LTE Lean Carrier
Ericsson
RAN #71, Göteborg, Sweden, March 7 - 10, 2016
AI 10.1.1
RP-160276

## Slide 2: Background
UEs of Rel-8 and beyond may expect CRS across the system bandwidth in every subframe
  High inter-cell interference even at low/medium load  Unnecessarily low per-user throughput
  Prevents eNB’s Power Amplifier from entering deep sleep  Unnecessarily high power consumption even at low/medium load
Rel-13: On an LAA* SCell the UE shall not expect any reference symbols other than DRS and other than in PDSCH transmission bursts  An LAA SCell is lean but available for unlicensed spectrum only
*) LAA: License Assisted Access

## Slide 3: WI Scope: Lean Carrier Reuse the LAA Carrier Design
Support “Lean PCell” as well as “Lean SCell”
Minimal changes & additions for “Lean SCell”
  e.g. capability signaling
Moderate changes & additions for “Lean PCell”
  MIB/SIB
  Random Access
  Radio Link Monitoring
  Extensions of the LAA reference signal design to operate with medium mobility scenarios

## Slide 4: Migration Backwards Compatibility
A Lean Carrier is not backwards compatible (due to lack of CRSs)
However, the Lean Carrier …
  may act as deactivated SCell for Rel-12 UEs (SCE-L1)
  may temporarily send full CRSs while used as SCell for pre-Rel-14 UEs
  may revert to legacy carrier operation when needed (e.g. if a neighboring legacy carrier can temporarily not handle all legacy UEs)
It is possible to introduce Lean Carrier step-wise and seamlessly if network operates with two or more carriers.
Benefits visible already during the migration