## Slide 1: Motivation for New WI: High-Performance eMTC (HeMTC)
Agenda item: 10.1.1
Source: Intel Corporation
Document for: Discussion
3GPP TSG RAN Meeting #71 RP-160531
Gothenburg, Sweden, 7th – 10th March 2016 rev of RP-150434

## Slide 2: Introduction
In Release 12: Category 0 UE and Power Saving Mode (PSM)
  Cat. 0 UE reduces the UE complexity and the peak data rate compared to Cat. 1 UE.
  PSM extends the battery life for devices with relaxed MT reachability requirements.
In Release 13: eMTC, eDRX and NB-IoT UE
  eDRX extends the battery life for devices with stricter MT reachability requirements.
  eMTC
    Cat. M1 UE reduces device complexity vs. Cat. 0 UE (e.g. simplifying features, 1.4 MHz BW operation).
    Cat. M1 reduces the peak data rate vs. Cat. 0 (e.g. around 300 kbps when operating in HD-FDD and 800 kpbs when operating in FD-FDD)
    Enhanced coverage (+15 dB over LTE).
  NB-IOT
    NB-IOT UE reduces device complexity vs. Cat. M1 UE (e.g. simplifying features, 180 kHz BW operation).
    NB-IOT reduces the peak data rate vs. Cat. M1 (e.g. around 200kbps)
    Support for extreme coverage (+20dB)
In Release 14: High-performance eMTC UE
  Support of VoLTE with no coverage loss compared to Cat. 1 LTE UE and
  Higher data rates (e.g., in the order of several Mbps)
  while getting the benefits introduced by Rel-13 BL MTC UEs (e.g., UE complexity reduction, support coverage enhancements) amongst others.
Notes: BL = Bandwidth reduced Low complexity
MT = Mobile Terminated calls

## Slide 3: Use Case Examples
MTC/IoT use cases for higher data rates and lower latency than Rel-13 eMTC and NB-IoT
(*)Source for use cases: Analysis Mason, 2015
Exemplary use cases are categorized
  Use cases that are optimally supported by NB-IOT or Cat M1
  Use case that might not be optimally supported by NB-IOT or Cat M1 due to the required support of voice or the data rate, e.g.:
  Wearables supporting voice or video connecting directly to the network without using the smart phone as concentrator.
  Health care requiring call feedback opportunities for emergency
  Tracking with voice to guide lost children or trouble shooting
  Surveillance to trigger voice or video for monitoring purposes
Notes: Why vending machine “red”?  high end vending machine where you need to be able to contact an help with the support of voice.
Why process and safety monitoring “green”?  I assume that this is safety for industrial control, so I would imagine examples like fire detector or level of for example irradiation in nuclear stations or level of chemical substances in a chemical industry which would switch on an alarm. Here I agree one could also consider cases when there is the need to support voice to help people evacuating certain areas for example.
Why location status “green”? OTDOA is not supported as of now. Any other LPP based positioning has been defined?  Isn’t it true that for Cat M1 there is positioning supported?
Why alarm system “red”? Any latency issue?  This is in the family of smart buildings so I would imagine an alarm system which send you in real time video when someone rings the bell and you are not at home, or that triggers a call so that you can answer even if you are not an home. So I assumed the support of voice.

## Slide 4: Measurement Results Cat 1 (DL)
Chart: 
| -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2
DL PRB | 25.5696 | 24.0294 | 20.6286 | 20.7889 | 16.7933 | 13.4219 | 10.8729 | 9.3241 | 8.1028 | 8.4027 | 5.6784
POLQA | 1.51 | 2.8305 | 2.745 | 2.5234 | 3.424 | 3.9028 | 3.934 | 3.942 | 3.9388 | 3.898 | 3.911 | 3.9486
right y axis
left y axis
Good POLQA, but > 6 PRB allocated
SNR
ETU70L
Scenario:
DL 2 RX; BW: 20 MHz
Each SNR point consists of 50 Harvard sentences (~ 50*10 sec.)
Averaging of POLQA and PRB allocation over 500sec. is done for each SNR point.
AMR-WB 12.65 kbps TBS 712 bits
  IPv4 (20 byte) + RoHC + C-DRX-40
Target Coverage: SNRTarget = –4 dB (R1-143769)
 For Cat 1, an allocation with up to a maximum of 6 PRB is only possible for SNR ≥ 2 dB.
~6dB
Cat M1 needs to enhance coverage by 11 dB to support AMR12.65 like with legacy LTE categories:
6 dB due to the lower number of PRBs in Cat. M1
5 dB due to the single antenna and the loss of frequency diversity in Cat M1
Therefore Cat M1 does not support VoLTE with the same coverage as for Cat 1
Notes: Harvard sentences are collection of sentences which are normally used to test the speech quality.
POLQA is the quality index, from 1 (very bad) to 5 (excellent). Good voice quality is around 3.5…4 or higher.

## Slide 5: Objectives
A new feature for a UE targeting higher data rate MTC/IoT applications as a (backward compatible) evolution of Rel-13 eMTC aiming to re-use the Rel-13 design
Primary objectives include:
  Enhancements to increase peak data rates and to improve support of delay sensitive services (such as VoLTE) compared to Cat-M1, e.g., AMR-WB requires a TBS of up to 2000 bits for voice packets with uncompressed IP headers (DRX-40)
    Increased values of maximum transport block size (TBS) for both DL and UL beyond those for Cat-M1
    HARQ-ACK bundling/multiplexing for HD-FDD to enhance peak data rates
    Wider than 1.4 MHz UE bandwidth at RF and scalable UE bandwidth at baseband within the maximum supported LTE system bandwidth
      UE BW at RF: Determine the maximum supported bandwidth considering power consumption, complexity, data rates, and latency
      UE BW at baseband: Enhance Rel-13 eMTC solution to enable scalable bandwidth support at the baseband (from 1.4MHz up to the maximum RF bandwidth) in RRC connected mode depending on data rate and latency requirements (e.g. for VoLTE) to effectively trade-off performance against power consumption and device complexity.
Notes: Rel 13 BL eMTC = Rel-13 Bandwidth reduced Low complexity eMTC = Cat. M1.

## Slide 6: Key Characteristics Summary (1/2)
Maximal reuse of Cat M1 design
  Cross-subframe scheduling
  No simultaneous reception of multiple TBs
  Limited support of transmission schemes and modes
  No dynamic scheduling for SI message transmissions
  Random access and paging support via “M-PDCCH” CSS instead of legacy PDCCH spanning entire LTE system BW
  HD-FDD with optimizations beyond Cat M1
  UE Requirements based on 1 RX
Advantages over Cat.1
  BW on demand for scalable data rate up to a maximum bandwidth within the maximum supported LTE system bandwidth
  Reduced complexity
  Reduced power consumption
Advantages over Cat.M1
  Higher data rates (several Mbps)
  Improve the support of delay sensitive services (e.g. VoLTE)
(1) Based on a maximum bandwidth of 5MHz, FD-FDD.
(2) 1.28s eDRX
  (3) DRX 40ms, (M-)PDCCH, on duration 4ms, inactivity timer 4ms, max. HARQ Tx 4, Band 4, speech activity 40/40/20
  (4) 0dBm, 6PRB PxSCH
(5) PDSCH: 18 PRB for 1-rx, 9 PRB for 2-rx (Cat 1), PUSCH: 6 PRB, 23 dBm
Cat. 1 | Estimation(1) | Cat. M1
100% | ~55% | 45%
 | Cat. 1 | Estimation(1) | Cat. M1
Idle(2) | 100% | ~65% | 60%
VoLTE (high SNR, normal coverage) (3,4) | 100% | ~55% | 55%
VoLTE (low SNR, low coverage) (3,5) | 100% | ~65% | NA

## Slide 7: Key Characteristics Summary (2/2)
36.888
Characteristics | Cat. 1 | Rel-12 Cat. 0 | Rel-14 HeMTC | Rel-13 Cat. M1
Peak data rates | DL/UL 10/5 Mbps | DL/UL 1/1 Mbps | DL/UL: no less than 3/2 Mbps(1) | 800kbps FD / ~300Kbps HD
Rx chains, layers | 2, 1 | 1, 1 | 1, 1 | 1, 1
BW | 1.4, 3, 5, 10, 15, 20 MHz | 1.4, 3, 5, 10, 15, 20 MHz | e.g.1.4, 3, 5 MHz | 1.4 MHz
Deployments | Standalone LTE channel, HD-FDD optional | Standalone LTE channel, HD-FDD optional | Standalone, LTE in-band, HD-FDD preferred | Standalone, LTE in-band, HD-FDD preferred
Max. modulation | DL 64-QAM, UL 16-QAM | DL 64-QAM, UL 16-QAM | e.g. DL 16QAM, UL 16-QAM | DL/UL 16-QAM
Max. UE Tx power | 23 dBm | 23 dBm | 20/23 dBm | 20/23 dBm
PSM, eDRX, mobility | connected mode mobility | connected mode mobility, PSM | eDRX, connected mode mobility, PSM | PSM, eDRX, connected mode mobility
Coverage, MCL | DL: 145.4 dB (20 kbps, FDD) UL: 140.7 dB (20 kbps, FDD) | DL: 145.4 dB (20 kbps, FDD) UL: 140.7 dB (20 kbps, FDD) | similar to Cat-M1 Mode A at least | target 155.7 dB (15 dB improvement) at least in certain conditions
LTE design | LTE | LTE | Cat M1 with enhancements to enable scalable bandwidth | repetition, M-PDCCH, X-SF scheduling
DL Scheduling | PDCCH, EPDCCH | PDCCH, EPDCCH | M-PDCCH with enhancements | M-PDCCH
Support of VoLTE | Yes | Yes (possible limitations) because of reduced TBS) | Yes | Limited support especially for HD-FDD
Complexity scaling [36.888] | 100% | ~55% [36.888](1) | ~55%(1) | ~45% (1)
(1)Comparison assumes FD-FDD