## Slide 1: Motivation for new SI on Interference cancellation receiver for LTE BS
China Telecom, Huawei
June, 2016
RP-160768

## Slide 2: Motivation for BS IC receiver
Importance of LTE UL throughput improvement
  With the wider usage of mobile applications like cloud services, social networking and point to point video/file sharing, UL traffic load is becoming much heavier.
LTE UL is interference limited in typical networks, and co-channel interference has substantial impact on UL cell average and cell edge throughput
  BS MMSE-IRC receiver can bring in significant SINR gain over MMSE receiver by suppressing the inter-cell interference, in both homogeneous and heterogeneous networks, as concluded in TR 36.884 [1].
  Consider the further evolution of BS receiver, such as interference cancellation (IC) receiver, to mitigate the inter-cell interference as well as the intra-cell inter-user interference.
MMSE
MMSE-IRC
IC
BS advanced receiver
Completed in June 2016
Proposed to be considered in Rel-14

## Slide 3: Target scenarios
Scenario 1: inter-cell interference scenario
The target cell and interference cell(s) are co-located or connected with ideal backhaul
Scenario 2: intra-cell inter-user interference scenario
Multiple users are co-scheduled on the same resource elements
  In scenario 1 and 2, full knowledge of interference parameters is available at the target cell.

## Slide 4: Potential gain by BS IC receiver (1/2)
In the inter-cell interference scenario (scenario 1), compared to MMSE-IRC receiver, BS IC receiver is expected to further improve the received SINR for cell center and cell edge UEs.
 | Interference level | (DIP1, DIP2) | Average MMSE-IRC gain over MMSE *** | Potential IC gain over MMSE ****
Homogeneous scenario | Low | (-5.55, -7.09) * |  | 2.79 dB
 | Medium | (-3.17, -7.03) * |  | 4.96 dB
 | High | (-1.11, -10.91) ** | 3.1 dB for 2Rx 4.4-4.7 dB for 4Rx 4.9-5.0 dB for 8Rx | 8.40 dB
Co-channel heterogeneous scenario | Low | (-4.73, -6.67) * |  | 3.49 dB
 | Medium | (-2.08, -7.17) * |  | 7.23 dB
 | High | (-0.43, -13.78) ** | 5.5-5.9 dB for 2Rx 7.5-8.3 dB for 4Rx 8.4-8.9 dB for 8Rx | 12.81 dB
Note* DIP values simulated by China Telecom. Note** DIP values averaged among 6 companies in Rel-13 BS MMSE-IRC WI [1]. Note*** MMSE-IRC gain averaged among 7 companies in Rel-13 BS MMSE-IRC WI [1]. Note**** Assuming that the two interferers are mitigated completely. |  |  |  | 

## Slide 5: Potential gain by BS IC receiver (2/2)
  Capacity region for joint decoding indicates the performance upper band for IC receiver.
  Joint decoding: decoding of all signals is performed simultaneously.
  Capacity region for independent decoding indicates the performance upper band for MMSE receiver.
  Independent decoding: different signals are decoded independently and in parallel.
Fig. Capacity regions for a two-user M-receiver system
In the intra-cell inter-user interference scenario (scenario 2), compared to MMSE receiver, BS IC receiver is expected to achieve noticeable throughput gain for cell center and cell edge UEs, based on the theoretical analysis [3].

## Slide 6: Proposal and scope
Proposal
  Start a RAN4-led SI in Rel-14 to study the performance benefits of BS IC receiver under typical deployment scenarios and with practical receiver implementation.
Scope
  Identify the target deployment scenarios and the co-channel inter/intra-cell interference conditions
  Identify the reference receiver structures for PUSCH
  Agree on the interference models, interference levels and simulation parameters for link level evaluations
  Evaluate the link-level gain for PUSCH over baseline receiver
    Evaluate the link-level gain over baseline Rel-13 MMSE-IRC receiver for inter-cell interference scenarios.
    Evaluate the link-level gain over baseline Rel-8 MMSE receiver for intra-cell inter-user interference scenarios.
  Note: the utilization of BS IC receiver is transparent to the users, and the performance gain of BS IC receiver can also be enjoyed by legacy users.

## Slide 7: References
[1] 3GPP RP-160766, “TR 36.884 V2.0.0: Performance requirements of MMSE-IRC receiver for LTE BS”, RAN #72, Jun 2016.
[2] 3GPP RP-150206, “Revised WID: Performance requirements of MMSE-IRC receiver for LTE BS”, RAN #67, Mar 2015.
[3] Bruno Suard, Guanghan Xu, Hui Liu, et al., “Uplink Channel Capacity of Space-Division-Multiple-Access Schemes,” IEEE transactions on information theory, vol. 44, no. 4, July 1998.

## Slide 8
Thanks!