## Slide 1: Motivation for New WI: High-Performance eMTC (HeMTC) for LTE
Agenda item: 10.1.1
Source: Intel Corporation
Document for: Discussion
3GPP TSG RAN Meeting #72 RP-160952
Busan, Korea, 13th – 16th June 2016 updated from RP-160531

## Slide 2: Introduction
In Release 12: Category 0 UE and Power Saving Mode (PSM)
  Cat. 0 UE reduces the UE complexity and the peak data rate compared to Cat. 1 UE.
  PSM extends the battery life for devices with relaxed MT reachability requirements.
In Release 13: eMTC, eDRX and NB-IoT UE
  eDRX extends the battery life for devices with stricter MT reachability requirements.
  eMTC
    Cat. M1 UE reduces device complexity vs. Cat. 0 UE (e.g. simplifying features, 1.4 MHz BW operation).
    Cat. M1 reduces the peak data rate vs. Cat. 0 (e.g. around 300 kbps when operating in HD-FDD and 800 kpbs when operating in FD-FDD)
    Enhanced coverage (+15 dB over LTE).
  NB-IOT
    Cat. NB1 UE reduces device complexity vs. Cat. M1 UE (e.g. simplifying features, 180 kHz BW operation).
    Cat. NB1 UE reduces the peak data rate vs. Cat. M1 (e.g. < 30 kbps)
    Support for extreme coverage (+20dB)
In Release 14: High-performance eMTC UE
  Support of use cases requiring higher data rates (audio/video streaming) and possibly also lower latency (e.g., VoLTE) with no coverage loss compared to Cat. 1 LTE UE while getting the benefits introduced by Rel-13 Cat M1 UEs (e.g., UE complexity reduction, support coverage enhancements) amongst others.
Notes: BL = Bandwidth reduced Low complexity
MT = Mobile Terminated calls

## Slide 3: Use Case Examples
MTC/IoT use cases for higher data rates and lower latency than Rel-13 eMTC and NB-IoT
(*)Source for use cases: Analysis Mason, 2015
Exemplary use cases are categorized
  Use cases that are optimally supported by Cat. M1 or Cat. NB1
  Use case that might not be optimally supported by Cat. M1 or Cat. NB1 UEs due to the required support of voice or the data rate, e.g.:
  Wearables supporting audio/video streaming
  Wearables supporting voice or video connecting directly to the network without using the smart phone as concentrator.
  Health care requiring call feedback opportunities for emergency
  Tracking with voice to guide lost children or trouble shooting
  Surveillance to trigger voice or video for monitoring purposes
Notes: Why vending machine “red”?  high end vending machine where you need to be able to contact an help with the support of voice.
Why process and safety monitoring “green”?  I assume that this is safety for industrial control, so I would imagine examples like fire detector or level of for example irradiation in nuclear stations or level of chemical substances in a chemical industry which would switch on an alarm. Here I agree one could also consider cases when there is the need to support voice to help people evacuating certain areas for example.
Why location status “green”? OTDOA is not supported as of now. Any other LPP based positioning has been defined?  Isn’t it true that for Cat M1 there is positioning supported?
Why alarm system “red”? Any latency issue?  This is in the family of smart buildings so I would imagine an alarm system which send you in real time video when someone rings the bell and you are not at home, or that triggers a call so that you can answer even if you are not an home. So I assumed the support of voice.

## Slide 4: Objectives
A new feature for a UE targeting higher data rate MTC/IoT applications as a (backward compatible) evolution of Rel-13 eMTC aiming to re-use the Rel-13 design
Primary objectives include:
  Enhancements to (i) increase peak data rates for unicast traffic, (ii) increase cell-edge DL data rates (e.g., target support of audio streaming rate of 64 kbps at DL SINR of -4.1 dB), and (iii) improve support of delay sensitive services (e.g.,VoLTE) compared to Cat-M1, e.g., AMR-WB requires a TBS of up to 2000 bits for voice packets with uncompressed IP headers (DRX-40)
    Increased values of maximum transport block size (TBS) for both DL and UL, and FDD, TDD, and HD-FDD beyond those for Cat-M1
    Wider than 1.4 MHz UE bandwidth at RF and scalable UE bandwidth at baseband within the maximum supported LTE system bandwidth
      UE BW at RF: Determine the maximum supported bandwidth considering power consumption, complexity, data rates, and latency
      UE BW at baseband: Enhance Rel-13 eMTC solution to enable scalable bandwidth support at the baseband (from 1.4MHz up to the maximum RF bandwidth) in RRC connected mode depending on data rate and latency requirements to effectively trade-off performance against power consumption and device complexity
      Support use of Rel-13 coverage enhancement techniques by non-BL UEs with greater than 1.4 MHz bandwidth support at the baseband in RRC connected mode [RAN1/RAN2].
    HARQ-ACK bundling/multiplexing for HD-FDD UEs and up to 10 DL HARQ processes for FD-FDD to enhance peak data rates
Notes: Rel 13 BL eMTC = Rel-13 Bandwidth reduced Low complexity eMTC = Cat. M1.

## Slide 5: Alternative solutions: A quick comparison (1/2)
Advantages of HeMTC over Cat. 1 and (hypothetical) Cat. 1 with 1Rx
  BW on demand for scalable data rates up to a maximum UE RF bandwidth within the supported LTE system bandwidth
  Reduced UE complexity
    Note: The complexity analysis above follows the framework in TR 36.888. It does not consider functionality-related device complexity (e.g., support of all Rel-8 mandatory features is needed for Cat. 1 and Cat.1 w/ 1 Rx, while this is not needed for Cat M1 or HeMTC). Thus, the actual complexity gap can be expected to be larger between HeMTC against Cat. 1 and Cat. 1 w/ 1Rx than shown above.
  Reduced UE power consumption
(1) Based on a maximum bandwidth of 5MHz. FD-FDD assumed for all options.
(2) 1.28s eDRX
  (3) DRX 40ms, (M-)PDCCH, on duration 4ms, inactivity timer 4ms, max. HARQ Tx 4, Band 4, speech activity 40/40/20
  (4) 0dBm, 6PRB PxSCH
(5) PDSCH: 18 PRB for 1-rx, 9 PRB for 2-rx (Cat 1), PUSCH: 6 PRB, 23 dBm
(6) Audio streaming at 64 kbps with enhanced coverage (i.e., @ low SNR) would not be feasible with Cat 1 w/ 1 Rx or Cat. M1
Cat. 1 | Cat.1 w/ 1Rx | HeMTC(1) | Cat. M1
100% | 75% | ~55% | 45%
Scenario | Cat. 1 | Cat.1 w/ 1Rx | HeMTC((1) | Cat. M1
Idle(2) | 100% | 85% | ~65% | 60%
VoLTE (high SNR, normal coverage) (3,4) | 100% | 75% | ~55% | 55%
VoLTE (low SNR, low coverage) (3,5) | 100% | 80% | ~65% | NA
Audio streaming (normal coverage)(6) | 100% | 75% | ~65% | 70%

## Slide 6: Alternative solutions: A quick comparison (2/2)
Other advantages of HeMTC over Cat. 1 and (hypothetical) Cat. 1 with 1Rx
  Support of use cases with higher data rates and lower latency with same coverage as Cat 1
    Cat.1 w/ 1Rx: No
    HeMTC: Yes
  Rel-13 enhanced coverage for > 6 PRBs
    Cat.1 & Cat.1 w/ 1Rx: No
    HeMTC: Yes
  HD-FDD support with lower complexity
    Cat.1 & Cat.1 w/ 1Rx: Type A HD-FDD
    HeMTC: Type B HD-FDD
  Reduced max UE RF BW:
    Cat.1 & Cat.1 w/ 1Rx: None
    HeMTC: Yes
  DL control channel monitoring
    Cat.1 & Cat.1 w/ 1Rx: based on legacy wideband PDCCH and larger number of BD attempts
    HeMTC: based on MPDCCH with reduced number of BD attempts
Advantages of HeMTC over Cat. M1
  Higher data rates (several Mbps)
  Improve the support of delay sensitive services (e.g. VoLTE)
  Larger TBS values to handle VoLTE packet re-transmissions without RoHC

## Slide 7: Key Characteristics Summary (1/2)
Maximal reuse of Cat. M1 design
  Cross-subframe scheduling
  No simultaneous reception of multiple TBs
  Limited support of transmission schemes and modes
  No dynamic scheduling for SI message transmissions
  Random access and paging support via “M-PDCCH” CSS instead of legacy PDCCH spanning entire LTE system BW
  (Type B) HD-FDD with optimizations beyond Cat M1
  UE Requirements based on 1 RX

## Slide 8: Key Characteristics Summary (2/2)
36.888
Characteristics | Cat. 1 | Rel-12 Cat. 0 | Rel-14 HeMTC | Rel-13 Cat. M1
Peak data rates | DL/UL 10/5 Mbps | DL/UL 1/1 Mbps | DL/UL: no less than 3/2 Mbps(1) | 800kbps FD / ~300Kbps HD
Rx chains, layers | 2, 1 | 1, 1 | 1, 1 | 1, 1
BW | 1.4, 3, 5, 10, 15, 20 MHz | 1.4, 3, 5, 10, 15, 20 MHz | e.g., one of: 1.4/3/5/10 MHz | 1.4 MHz
Deployments | Standalone LTE channel, HD-FDD optional | Standalone LTE channel, HD-FDD optional | Standalone, LTE in-band, HD-FDD preferred | Standalone, LTE in-band, HD-FDD preferred
Max. modulation | DL 64-QAM, UL 16-QAM | DL 64-QAM, UL 16-QAM | e.g. DL 16QAM, UL 16-QAM | DL/UL 16-QAM
Max. UE Tx power | 23 dBm | 23 dBm | 20/23 dBm | 20/23 dBm
Mobility | Connected mode mobility | Connected mode mobility | Connected mode mobility | Connected mode mobility in CE Mode A
Coverage, MCL | DL: 145.4 dB (20 kbps, FDD) UL: 140.7 dB (20 kbps, FDD) | DL: 145.4 dB (20 kbps, FDD) UL: 140.7 dB (20 kbps, FDD) | Similar to Cat-M1 Mode A at least | target 155.7 dB (15 dB improvement) at least in certain conditions
LTE design | LTE | LTE | Cat M1 with enhancements to enable scalable bandwidth | repetition, M-PDCCH, X-SF scheduling
DL Scheduling | PDCCH, EPDCCH | PDCCH, EPDCCH | M-PDCCH with enhancements | M-PDCCH
Support of VoLTE | Yes | Yes (possible limitations) because of reduced TBS) | Yes | Limited support especially for HD-FDD
Complexity scaling [36.888] | 100% | ~55% [36.888](1) | ~55%(1) | ~45% (1)
(1)Comparison assumes FD-FDD

## Slide 9: Appendix

## Slide 10: Measurement Results Cat 1 (DL): A Case study for VoLTE
Chart: 
| -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2
DL PRB | 25.5696 | 24.0294 | 20.6286 | 20.7889 | 16.7933 | 13.4219 | 10.8729 | 9.3241 | 8.1028 | 8.4027 | 5.6784
POLQA | 1.51 | 2.8305 | 2.745 | 2.5234 | 3.424 | 3.9028 | 3.934 | 3.942 | 3.9388 | 3.898 | 3.911 | 3.9486
right y axis
left y axis
Good POLQA, but > 6 PRB allocated
SNR
ETU70L
Scenario:
DL 2 RX; BW: 20 MHz
Each SNR point consists of 50 Harvard sentences (~ 50*10 sec.)
Averaging of POLQA and PRB allocation over 500sec. is done for each SNR point.
AMR-WB 12.65 kbps TBS 712 bits
  IPv4 (20 byte) + RoHC + C-DRX-40
Target Coverage: SNRTarget = –4 dB (R1-143769)
 For Cat 1, an allocation with up to a maximum of 6 PRB is only possible for SNR ≥ 2 dB.
~6dB
Cat M1 needs to enhance coverage by ~10 dB to support AMR12.65 like with legacy LTE categories:
6 dB due to the lower number of PRBs in Cat. M1
3-4 dB due to the single antenna in Cat M1
Therefore Cat M1 does not support VoLTE with the same coverage as for Cat 1
Notes: Harvard sentences are collection of sentences which are normally used to test the speech quality.
POLQA is the quality index, from 1 (very bad) to 5 (excellent). Good voice quality is around 3.5…4 or higher.