## Slide 1: Motivation for Enhanced SU-MIMO Performance requirement for LTE
LG Electronics
3GPP TSG-RAN Meeting #73
New Orleans, USA, September 19 - 22, 2016
Document for: Information
Agenda Item: 10.1.4
RP-161498

## Slide 2: Background
Rel-12 SU-MIMO WI
  SU-MIMO WI was covered
    2X2 antenna configuration
    Dual layers
    Up to 64QAM.
  Reference receivers are Reduced ML(R-ML) and CWIC.
  Performance requirements were defined by R-ML regarding minimum performance rule.
Rel-13 4RxAP WI
  4RxAP WI considers
    2X4 and 4X4 antenna configurations
    Up to four layers
    Up to 256QAM
  Reference receiver is MMSE(-IRC).

## Slide 3: Motivation
  4X4 antenna configuration will be widely deployed in real network
  To support higher layer and 256QAM with MMSE receiver
    Target geometry is too high
    Link and system level performances are limited in real network deployment
Limited use case for four layers in real network

## Slide 4: Proposal WI
  Performance for four layer and 256QAM with advanced receiver
    R-ML provides performance improvement in comparison with MMSE
New performance requirements of enhanced SU-MIMO for LTE is required
  Candidate reference receivers
    R-ML
  Supporting
    Up to four layers
    Up to 256QAM
    2X4 and 4X4 antenna configurations