## Slide 1: Outlook on Rel-15 NB-IoT enhancements
3GPP TSG RAN Meeting #74 RP-162160
Vienna, Austria, December 5-8, 2016
Agenda Item: 10.1.1
Source: Huawei, HiSilicon, Neul
Document for: Information

## Slide 2: Justification
Rel-14 will introduce 6 new features
  Positioning, multicast, non-Anchor PRB enhancements, mobility and service continuity enhancements, new Power Class(es), power consumption and latency reduction
IoT marketplace is fast changing with newly-emerging opportunities that cannot always be predicted. It is essential that NB-IoT takes every chance to give 3GPP and operators the maximum opportunity to adapt, and offer ultra-low cost IoT to new customers and applications
It is important to further enhance NB-IoT in Rel-15:
  Support new deployment scenarios, such as TDD and unlicensed spectrum, standalone and guard-band/in-band combination in a multi-PRB deployment, small cell deployment
  Further reduce the power consumption and latency, especially the power consumption and latency for downlink command
  Enhance the performance for standalone and guard-band in order to smoothly evolve to 5G mMTC
  A new category to support higher peak data rate

## Slide 3: Objectives (1/4)
Further latency and power consumption reduction
Reduce the latency and power consumption for downlink data transmission [RAN1, RAN2]
Support SR in the physical layer [RAN1, RAN2]
Contention-based access (in licensed UL spectrum), e.g, RACHless transmission with existing 3.75kHz/15kHz waveforms [RAN2, RAN1]
Higher layer optimization
  Fast RRC release [RAN2]
  Identify and support scenarios with reduced need for IDLE mode UE measurements [RAN2]

## Slide 4: Objectives (2/4)
A new category to support higher peak data rate
In a new NB-IoT UE category, support carrier aggregation operation on up to [8] contiguous NB-IoT carriers [RAN1,RAN2, RAN4]
Support for small cell NB-IoT deployment [RAN2, RAN1]
Study (if needed) and support up to 8 hops between the originating UE and the destination eNB, all hops over NB-IoT
Necessary changes to allow the increased time to transfer a message

## Slide 5
Support for different QoS
Define necessary enhancements to the Subscriber Profile ID (SPID) to enable identification of the requirements of use cases including at least coverage enhancement, PSM/eDRX, and QoS [RAN3]
Enable X2/S1 transfer of NB-IoT QCI [RAN3]
Enhancements to standalone operation mode
Use of all DL OFDM symbols for all physical channels and signals [RAN1]
Signalling and requirements to support multi-carrier operation for (a) standalone anchor with in-band/guard-band non-anchor and (b) standalone non-anchor with in-band/guard-band anchor carriers [RAN2, RAN4]
Objectives (3/4)

## Slide 6: Objectives (4/4)
Support for TDD
Separate documents are provided
Motivation: RP-162161
Licensed-downlink assistance with unlicensed uplink for NB-IoT
Separate documents are provided
SID: RP-162158
Motivation: RP-162159

## Slide 7: Further power consumption and latency reduction
Motivation
  In downlink command/data transmission, the latency is dominated by eDRX cycle, and the power consumption is dominated by the eDRX cycle and the paging.
  NB-IoT can support long battery life for 2 minutes latency with about 25 uA average power consumption in 144 dB MCL.
Proposed solution
  Dedicated paging indication signal/channel with much shorter decoding time of receive circuit than paging decoding
  Introduce a new state which is between idle state and active state. The UE performs in this new state the same as in idle state except monitoring paging indication(PI) signal/channel instead of paging. When the UE detects the PI, it monitors the paging according to Paging Opportunity (PO).

## Slide 8
Motivation
  In small packet transmission, signaling consumes significant over-the-air resources, leading to larger delay and lower device battery life.
  Emergency reports are very high priority when they do need to be sent, so benefit from shorter latency by reducing signaling.
  Example applications include fire alarm sensor, water leakage sensor, etc.
Design principle
  Reduced signaling before uplink data transmission to reduce the transmission delay, e.g., RACH-less transmission
  Allocate dedicated time-frequency resources for contention based uplink access
Contention-based uplink access (1/2)

## Slide 9
Example of solution
  No uplink TA, the uplink transmission is based on downlink synchronization; longer CP can be used to avoid interference between users.
  Coarse levels of MCS are supported to improve the capacity. Downlink measurements can be a reference for uplink MCS.
  Single tone transmission is enough for small traffic applications
  ACK/NACK of NPUSCH is helpful for better quality of services
  Open loop power control to mitigate the interference
  Space diversity is applied to mitigate the interference
  Contention resolution techniques need to be considered
  Supported in both RRC idle state and RRC connected state
Long CP
Data
Long CP
Data
Long CP
Data
UE1
UE2
UE3
Orthogonal multiple access
Contention-based uplink access (2/2)

## Slide 10: Small-cell deployment with NB-IoT backhaul
Motivation：
  In some scenarios, e.g. UEs deep underground may not be able to connect to NB-IoT macro eNB. However, the end user requires 100% coverage services. Small cells with multi-hops should be used in this scenario.
  NB-IoT macro cell and small cell provides a continuous wireless connection solution, so the UEs only need to support NB-IoT, which greatly reduces the cost of deployment.
Key technologies:
  Frequency allocation for small cell: NB-IoT bandwidth is only 200 kHz, it is assumed that each small cell uses different frequencies which facilitates the deployment of NB-IoT mesh network.
  Cell selection: UE can based on the radio condition and load information to choose the right small cell;

## Slide 11: SR in the physical layer
Motivation and background
  No SR in physical layer in NB-IoT. RACH Msg3 is used to carry higher-layer SR.
  When the UE is RRC active and has periodic data to transmit, the UE needs to initiate RACH or wait for an UL grant. Such a procedure either uses more RACH resources or imposes extra latency and
Solution
  Introduce SR in the physical layer and RAN2 support related enhancement
LTE
NB-IoT