## Slide 1: WI on critical communication in LTE
Motivation for new proposed WI Ericsson
RAN #74, Vienna, Austria, December 5-8, 2016
AI 10.1.1
RP-162041

## Slide 2: Reliability and latency
The 5G landscape consists of overlapping use cases based on
  eMBB (human user)
  mMTC (machine user)
  URLLC (reliability and latency)
While eMBB and mMTC are being addressed by LTE, URLLC is outside the current capability
  LTE should be improved for URLLC use cases within reach
5G use cases in LTE

## Slide 3: Justification
LTE part of 5G radio access
  Enabling new URLLC use cases
    Smart grid
    Remote (haptic) operation
    Process automation
    Factory automation
  Requirements for URLLC (3GPP/ITU)
    Reliability (10-5 error within 1ms, 32B packet)
    Ultra low latency (<0.5ms end-to-end)
Improving further on latency reduction work from
  Short TTI design from Rel-15
  Instant uplink access design from Rel-14

## Slide 4: WI Objectives
Aiming at wide area deployments, such as sensors and alarms
  Latency in a range from 10-100ms and configurable reliability level below 10-3
  FS1 and FS2, based on 1ms TTI
Aiming at local critical deployments, such as factories
  Supporting 3GPP 5G Reliability requirement
  FS1 based on short TTI
Improvements for UL and DL, in connected mode
Backwards compatible solutions
  Using existing LTE channel codes

## Slide 5: Technical Solutions
Semi-persistent scheduling enhancements in UL/DL
  Repetition factor to provide high reliability
  Contention based access to support many users
Robust data channel coding based on Turbo (figure)
  Repetitions, spatial diversity, CA
Robust control channels
Higher layer data duplication
  Reliable feedback
Repetitions of short TTIs with accumulated code rate, 344b block size

## Slide 6: Conclusion
LTE Rel-15 should address the reliability use cases within reach, supporting:
  High reliability for 1ms TTI with low to medium latency
  High reliability for short TTI with ultra-low latency
ITU targets for 5G URLLC should be fulfilled in LTE