## Slide 1
NR-based Access to Unlicensed Spectrum
RP-170205
3GPP RAN #75
Dubrovnik, March 2017
Qualcomm

## Slide 2: Background
3GPP has defined mechanisms to exploit unlicensed spectrum in conjunction with LTE
  LTE-WLAN Aggregation (LWA in Rel-13, eLWA in Rel-14)
  LAA family (LAA in Rel-13, eLAA in Rel-14)
    LAA has enabled Gbps LTE modem commercial implementations
Time has come for NR to tackle unlicensed spectrum
  From NR SID:
    “3GPP has to identify and develop the technology components needed for successfully standardizing the NR system timely satisfying both the urgent market needs, and the more long-term requirements set forth by the ITU-R IMT-2020 process. Further, the NR system should be able to use any spectrum band ranging at least up to 100 GHz that may be made available for wireless communications even in a more distant future.”
3GPP and unlicensed operation

## Slide 3: NR-unlicensed
Take NR system to unlicensed spectrum to
  Unlock access to more spectrum earlier for MNOs
  Open up cellular technologies to existing and new entities/markets/verticals,
    e.g., private networks, industrial automation, replacing wires with wireless connectivity
Objectives

## Slide 4: Why NR in unlicensed?
Wideband by design
Large range of Frequency bands: sub-6 and mmW
Flexible TDD from the beginning
Granular access: shorter “subframes”
Reduced latencies: shorter TTIs and self-containable subframes
Latest coding advancements
LTE coverage
All these features will directly benefit NR operation in unlicensed bands
  Lower wideband complexity implementations
  More dynamic medium access while retaining coverage set forth by LTE
5G NR “Heritage”

## Slide 5: Modes of Operation
Licensed Assisted Access (LAA) operation
  Requires licensed anchor carrier (LTE or NR)
    LTE anchor: aggregation of unlicensed spectrum as done in regular NSA NR operation, i.e., DC
    NR anchor: aggregation of unlicensed spectrum as done in regular SA NR operation (DC/CA as defined by NR WI)
    Neither of them requires special architectural treatment vis-à-vis regular licensed operation
    Definition of DC-based aggregation imposes the definition of all the PHY channels for the unlicensed carrier
      Similar to the NSA/SA discussion for regular licensed operation where all the PHY channels are required in NSA definition [PBCH being the only debatable PHY channel addition required for NSA support]
      Therefore, from PHY layer perspective, the same study applies to LAA and SA modes of operation
Stand-alone (SA) unlicensed operation
  SA requires definition of all procedures for unlicensed carrier
    e.g., Idle Mode procedures, Paging, SI delivery
  but makes it possible to operate the system without a licensed carrier (SA network architecture)
LAA and SA

## Slide 6: Proposal
Start SI for NR-unlicensed
  Leverage NR definition (PHY channels and procedures) to the maximum extent
  Leverage architecture options devised for regular (licensed) operation
Exploit forward compatibility hooks to address the special needs of medium access in unlicensed bands
Consider sub6 as well as mmW unlicensed bands
  Leverage coexistence work done for LAA for 5GHz band
  Companion contribution (RP-170207) proposes to:
    either start TR surveying unlicensed bands or extending the existing 60GHz TR (38.805) to cover other bands
SID attached