## Slide 1
Motivation for new Study Item on Ultra Reliable Low Latency Communication Enhancements for NR
RP-170229
RAN#75
Dubrovnik, Croatia, March 6 - 9, 2017

## Slide 2
Motivation (1/2)
URLLC requirements for NR in TR38.913
  <= 0.5ms for DL and UL user plane latency (without high reliability requirement)
  Reliability of 10-5 for 32-byte packet with a user plane latency of 1ms
In addition, it is necessary for NR to support a wide range of latency/reliability/mobility requirements for various URLLC applications.
Status of URLLC in NR SI
  There have been some limited agreements on how to support URLLC in NR, in the areas of such as mini-slot, URLLC/eMBB multiplexing in DL and UL, DL control channel reliability enhancement, grant-free UL transmissions.
  A lot of details are still open regarding these features.
  Most likely the agreed features are not sufficient to meet all the URLLC needs. This needs to be further investigated.
The URLLC study in the NR SI does not provide a clear view on all the components necessary to support URLLC, which deserves further investigation.

## Slide 3
Motivation (2/2)
Possible URLLC components in Rel-15 NR WI (to be discussed in RAN#75)
  Mini-slot
  High reliability of DL control channel (e.g. compact DCI, larger aggregation level)
  The enhancements to support URLLC using eMBB resources in DL
  Grant-free UL transmission (? If yes, to what extent?)
Not necessarily all the features agreed in the NR SI will be included to the full extent in Rel-15 NR WI due to the time constraint. (to be discussed in RAN#75)
It is unlikely Rel-15 NR WI will have spare time to investigate and identify further options necessary for URLLC.
A study item on URLLC in Rel-15 targeting specification work in Rel-16 is necessary.

## Slide 4
Phased Approach for the Proposed SI
Phase 1: a short phase analyzing the foreseen capabilities of the NR Rel-15 specifications to meet the URLLC needs based on the agreed WID
  This is not expected to take into account the detailed design in the NR WI, because the details will not available until a late stage.
Phase 2: identify the candidate solutions improving the URLLC support
  Initially the SI can focus on the aspects that do not rely on the detailed design in the NR WI
  The detailed design in the NR WI can be gradually taken into account as it becomes clearer.
  The aspects that can be considered includes e.g.
    Improved reliability of control and data channels
    Further latency enhancements
    Mobility enhancements