## Slide 1: Motivation for New WI proposal on enhancements of Light connection for LTE
Section 10.1.2
Intel Corporation, Huawei, China Telecom
3GPP TSG RAN Meeting #75 RP-170397 Dubrovnik, Croatia, March 6-9, 2017

## Slide 2: Background: NR Inactive “state”
Signalling reduction over the radio during Inactive to Connected transitions.
Reduced latency during Inactive to Connected transitions
Signaling reduction due to Paging and update messages.
Battery savings in UE from signalling reduction and reduced latency
Signalling reduction to CN over NG-C/U interfaces due to mobility and state transitions by hiding them from CN.

## Slide 3: Background: Solution details for NR Inactive
Storing UE AS context in RAN.
RAN initiated paging
RAN based notification area update mechanism
Hiding UE’s transition to Inactive from CN
UE context storage and retrieval along with UE mobility across different RAN nodes.

## Slide 4: Background: Rel-14 LTE Light RRC Connection
The feature offers similar benefits and functionalities to NR Inactive.
  The solution details are also almost identical.
Note that Rel-14 Light RRC Connection WI is for LTE eNB connected to EPC

## Slide 5: LTE eNB Connected to NG Core
When LTE eNB is connected to NG Core:
  Light RRC Connection functionality should be enhanced to inter-work with NG Core over NG-C/U interfaces
  Light RRC Connection functionality should be enhanced to inter-work with NG NAS in UE

## Slide 6: Potential enhancements
NR Inactive may offer additional optimisations; e.g.,
  Optimised Resumption
  Paging optimizations and Paging failure recovery
  Use of Access class barring and congestion control
  Optimised transition back to RRC Inactive
  Optimised transition from LTE Light connection to NR Inactive
  Possible data transmission in RRC Light Connection state
Many of these were also discussed in LTE Light RRC Connection but delayed due to lack of time
LTE Light RRC Connection should be enhanced to consider at least the same functionality and optimisation as NR Inactive

## Slide 7: Rel-15 WI Objectives
The objectives of this work item are:
  Enhance LTE Light RRC Connection to inter-work with NG NAS (RAN2)
  Enhance LTE Light RRC Connection to inter-work with NG Core (RAN3/RAN2)
  Enhance LTE Light RRC Connection to provide parity in terms of functionality, signalling and delay reduction to Inactive state in NR when LTE eNB is connected to NG Core (RAN2/RAN3)
    These enhancements can also be considered where applicable for LTE eNB connected to EPC
The solution should build on the Rel-14 Light RRC Connection functionality in LTE connected to EPC and minimise changes to radio interface.