## Slide 1: Motivation of UE Wakeup Mechanism in NR
CATT
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, Mar 6 – 9, 2017
RP-170410

## Slide 2: NR System Design - UE Power Saving
UE power saving had been considered in the beginning of NR system design
  System design considers UE power consumption
Most UE power consumptions are on the system monitoring for potential data arrival
  IDLE mode UEs: UE will wake up periodically to decoding paging indication and retrieve paging information based on configured DRX cycle
  CONNECTED mode UEs - active state PDCCH decoding dominate power consumption in LTE[Ref: R1-166368 UE Power Consideration based on Days-of-Use, Qualcomm]
    UE decodes PDCCH every subframe with most of time no grant for its transmission
    High speed network access and robust data arrival have the results of no one is scheduled for services in large fraction of time.
    Time of usage – quiet time in the night.

## Slide 3: NR Power Saving features
NR-PDCCH monitoring – RAN1#86bis agreements
  UE-specific DL control information monitoring occasions at least in time domain can be configured
    Network could configure longer duration for NR-PDCCH monitoring to reduce the power consumption on monitoring
RAN1# 86 agrees on the study of UE power saving
  Impact of UE DL reception energy consumption should be studied also considering the total power consumption mainly focusing on DoU
    e.g., UE decoding power consumption in the physical layer DL control blind decoding in lack of grant
    e.g., UE decoding power consumption in the slot with the data
    e.g., UE decoding power consumption in the data reception process
    e.g., UE decoding power consumption in the measurement
    e.g., UE decoding power consumption in the SS
  UE power reduction techniques also should be studied
Enhance DRX – support multiple service with different service requirements

## Slide 4: UE Power Saving with On-demand Access
On-demand Access – UE remains in sleeping mode unless it is triggered
  UL data arrival from higher layer: UE will wake up and request for UL transmission
  Wakeup by network – Network wakes up UE on demand
    Arrival of DL data
    System information change
Power saving –
  UE wakes up only being triggered by wakeup signals with extended sleeping mode
DL data
t
Wakeup signals
Sent by gNB
UE waking up
Paging
PDCCH decoding
PDSCH decoding
Complete data reception
UE backs to sleep
UE sleeping
UE sleeping

## Slide 5: UE Wakeup Signals
Wakeup signal receiver – a front-end device with low or no power consumption
  Low power circuit
  Passive circuit: similar to RFID or ETC (Electrical Toll Collection) receiver
    Backscattering technology –
      Highly reactive RF front end to stimulate the electromagnetic wave of the received signals from the gNB. The
      RF power is converted into DC power to power the control logic of wakeup trigger

## Slide 6: UE Wakeup Mechanism
Wakeup beacon – narrow band signals and waveform with high transmitted power
  NR physical channel structure
    Inband or out-of-band physical channel
  Wakeup strategy
  Multi-cell broadcast mechanism
Paging and DRX enhancement with UE wakeup signals
  Paging channel and paging mechanism along with reception of wakeup signals
  Enhanced DRX – extended UE sleeping cycle with wakeup signals
    Consideration of UE mobility

## Slide 7: Conclusion
On-demand access provides an mechanism for UE power saving
  UE wakeup mechanism to wake up UE right after data arrival
    Minimizing UE periodic wakeup to check for paging or data arrival
    Reducing PDCCH monitoring
    Optimizing DRX
  Study of UE wakeup mechanism
    Wakeup signal and waveform design
    Channel design and operation
    Enhancement of paging and DRX