## Slide 1: Motivation for SI on Scheduling enhancements with carrier aggregation for UMTS
Huawei, HiSilicon
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, Mar 6 – 9, 2017
Document for: Discussion
Agenda Item: 11.1
RP-170661

## Slide 2: DB-DC for HSDPA
HS-SCCH
HS-PDSCH
HS-SCCH
HS-PDSCH
900MHz
2.1GHz
Scenarios:
Along with the basic frequency for MBB coverage being in a lower band, e.g. 900MHz, carrier aggregation of two carriers in a lower band and a higher band (cross band carrier aggregation on e.g. 900MHz and 2.1GHz), would become a typical deployment scenario for multi-carrier application.
Problem description:
As one of typical scheduling channels, HS-SCCH is used to carry control information for HS-PDSCH demodulation and decoding. UE should firstly decode HS-SCCH before HS-PDSCH decoding. However, in DB-DC-HSPA feature reliability of HS-SCCHs on different carriers are different. Obviously HS-SCCH on primary carrier is more reliable than the secondary carrier in case of same transmission power.
Under the same detection performance requirement, HS-SCCH on the secondary carrier will require more power which leads to limitation to data transmission on HS-PDSCH.
The same issue will also happen on other downlink control channels like E-AGCH, E-RGCH or E-HICH.

## Slide 3: SI objectives
Identify the reliability issue of scheduling channels over the secondary carrier for cross band carrier aggregation and investigate mechanisms to improve the reliability.
  Study the reliability of scheduling channels over the secondary carrier, e.g. the coverage difference, detection performance, under different carrier aggregation scenarios.(RAN1)
  Investigate potential enhancement schemes to improve the reliability of scheduling channels over the secondary carrier, and identify the impacts on current specifications for introducing such enhancements.(RAN1, RAN2)

## Slide 4: WI time budget
RAN | R1 | R2 | R3 | R4RF | R4RD | R6 | R1 | R2 | R3 | R4RF | R4RD | RAN | R1 | R2 | R3 | R4RF | R4RD | R6 | RAN
75 March 17 REL-14 freeze | 88bis | 97bis | 95bis | 82bis | 82bis | 4 | 89 | 98 | 96 | 83 | 83 | 76 June 17 | 90 | 99 | 97 | 84 | 84 | 5 | 76 Sep 17
 | 2 | 1 |  |  |  |  | 2 | 2 |  |  |  |  | 1 | 1 |  |  |  |  |