## Slide 1: Motivation for TCP enhancement in NR

## Slide 2: Motivation
NR Rel-15, mainly designed for eMBB, is well-suited for DL TCP transmission.
  However, NR Rel-15 is not optimized for UL TCP ACK transmission.
NR aims at DL TCP throughput of ~20 Gbps...
  However, actual throughput in TCP layer is much less than 20 Gbps due to limitation by TCP ACK in UL.
QUIC is emerging transport layer protocol for enhancing IP throughput
  However, standardization work of QUIC is still ongoing in IETF. It is foreseen that QUIC cannot replace TCP in a near future.

## Slide 3: Motivation
TCP enhancement was already discussed in several RAN2 meetings in NR Rel-15
  However, RAN2#97bis finally concluded that this feature is not included in Rel-15 due to overload situation in RAN2.
Therefore, to maximize the DL TCP throughput, UL TCP ACK prioritization should be studied in NR Rel-16.

## Slide 4: Potential enhancement for TCP ACK prioritization
Prioritized TCP ACK processing in the transmitter side
  Head-of-line blocking problem of TCP ACK should be addressed.
  Mechanism can be considered in SDAP/PDCP/RLC/MAC depending on the targeted granularity for TCP ACK prioritization.
    E.g. Radio Bearer level, RLC bearer level, Logical channel level, etc.
Low latency TCP ACK transmission in the radio interface
  Scheduling and resource allocation enhancement for TCP ACK.
Prioritized TCP ACK processing in the receiver side
  Out-of-order delivery for TCP ACK.

## Slide 5: Proposals
Start the WI on TCP enhancement
  TCP ACK prioritization should be studied.
  TCP ACK thinning can also be studied.
  It could be part of NR_Voice, or studied as a separate item.
Mechanisms proposed in Rel-15 can be re-studied
  In addition, a new mechanism can also be studied.