## Slide 1: WF on SDL and SUL pairings
Huawei, AT&T, Deutsche Telekom, Orange, Telecom Italia, Vodafone
3GPP TSG RAN Meeting #80
La Jolla, USA, 11th June – 14th June 2018
RP-181361

## Slide 2: Background
Conclusion from RAN2
  “RAN2 has the understanding that the current RRC signalling would support configuring a serving cell with one downlink and one uplink carrier on different bands using the fields frequencyInfoDL and the uplinkConfigCommon=>frequencyInfoUL in ServingCellConfigCommon. It is up to RAN4 whether they intend to define such band combinations or whether there are any non-signalling related problems”
Open question
  SUL configurations (such as supplementaryUplinkConfig below) is only supposed to be signaled conditioned on ServCellAdd-SUL. Even if the UE would have only one choice of uplink from the SIB as in the conclusion from RAN2, all RAN2 specs always use SUL to explain what is applied to SUL, but it is not clear whether UE can receive SUL configurations under normal UL operation, and this would prevent applying SUL configurations such as for power control.
-- ASN1START
-- TAG-SERVING-CELL-CONFIG-COMMON-START
ServingCellConfigCommon ::= SEQUENCE {
physCellId PhysCellId OPTIONAL, -- Cond HOAndServCellAdd,
downlinkConfigCommon DownlinkConfigCommon OPTIONAL, -- Cond InterFreqHOAndServCellAdd
uplinkConfigCommon UplinkConfigCommon OPTIONAL, -- Cond ServCellAdd-UL
supplementaryUplinkConfig UplinkConfigCommon OPTIONAL, -- Cond ServCellAdd-SUL
n-TimingAdvanceOffset ENUMERATED { n25600, n39936 } OPTIONAL,-- Need S
...
}
-- TAG-SERVING-CELL-CONFIG-COMMON-STOP
-- ASN1STOP

## Slide 3: Proposal
Allow the release-independent definition of SDL+SUL band combinations for Rel-15 and later UEs
  Task RAN2 and RAN4 to double check if complete support for SDL+SUL in Rel-15 is already ensured, and if needed to complete the specifications for allowing configuration of a cell where the only UL signaled in SIB is in a RAN4-defined SUL band, and where the DL is in a RAN4-defined SDL band or in a TDD band. PRACH transmissions initiated only on the SUL should be supported.
  RAN2 and RAN4 to coordinate as needed.