## Slide 1: Summary of discussion on supported number of MIMO layers
Qualcomm
RP-181448
3GPP TSG RAN #80
La Jolla, CA, U.S.A., June 11 - 14, 2018
Agenda item 9.8

## Slide 2: Background
Feature 2-3 in the NR UE Feature list (RAN-1) :
2-3 | PDSCH MIMO layers | 1. Supported maximal number of MIMO layers | 2-1 | Yes | Only one layer is supported | Type 3 | N.A. | N.A. |  |  | RAN1 | Candidate values: {1,2,4,8} FFS on the minimal layers for different band or band combination. | 

## Slide 3: Discussion outcome / Proposal
Text proposal for last column in UE Feature 2-3
For single CC standalone NR, it is mandatory with capability signaling to support at least 4 MIMO layers in the bands where 4Rx is specified as mandatory for the given UE and at least 2 MIMO layers in FR2. Some relaxations to this requirement may be applicable in the future (including in Rel-15). Mandatory in all cases above means mandatory with capability signaling. It is not expected that there is a signaling change resulting from this (i.e. signaling remains to be defined as {1, 2, 4, 8} in every band, including FR1 and FR2.