## Slide 1: Power class related to UL MIMO
Huawei, HiSilicon
3GPP TSG RAN meeting #87e RP-200280
Electronic Meeting, March 16-19, 2020

## Slide 2: Content
Power class status in Rel-15
Identified issues in RAN4 for Rel-15
Proposals to address issues for Rel-15
Consideration for power class in Rel-16

## Slide 3: Power class status in Rel-15
SA
  Power class is a per band capability which does not distinguish MIMO or non-MIMO mode (single antenna port)
  RAN4 agreed in #89 that the power class should be the same for a UE supporting UL MIMO while configured to single antenna port mode
NSA
  Ambiguity exists for the power class of NR band in a band combination
  Rel-15 RAN4 spec
    Clarification was made in TS 38.101-3 that allows UE supporting UL MIMO in SA mode to fulfil either PC3 or PC2 requirements in NSA for the NR band
  Rel-16 RAN4 spec
    The clarification is not applicable for Rel-16 spec.

## Slide 4: Identified issues in RAN4 for Rel-15
For both SA and NSA modes, the issues root from the UE implementation architecture of 23dBm+23dBm to support PC2 UL MIMO, and this kind of UE are widely available in the market
  SA
    Same power class for both MIMO and non-MIMO mode may not be guaranteed for some UE
      To keep the power class unchanged, Tx div is the only way to reach 26dBm MOP for 23+23dBm PA architecture. However, Tx div may not be implemented for some UEs in Rel-15
  NSA
    Power class for a NR band in SA and NSA mode could be different due to implementation architecture
      The issue of possible different power class for a NR band in NSA band combination was tentatively solved in Rel-15 by clarification in RAN4 spec

## Slide 5: Proposals to address issues for Rel-15
Keep the principle that power class is unchanged for both MIMO and non-MIMO in SA mode.
Based on the principle, for UE supporting UL MIMO with 23dBm+23dBm PA configuration in single antenna port mode
  Define a transition period in RAN5
    For UE supporting Tx Div, PC2 requirements of 6.2.1 in TS 38.101 shall apply
    For UE not supporting Tx Div, PC3 requirements of 6.2.1 in TS 38.101 shall apply
  After that transition period, only PC2 requirements of 6.2.1 shall apply
  How to design the test case should be further discussed in RAN5

## Slide 6: Consideration for power class in Rel-16
SA
  No new power class should be introduced in Rel-16 to distinguish MIMO and non-MIMO mode
    It is worth noting that even new MIMO power class is introduced, it cannot solve the possible misalignment of power class between SA and NSA
NSA
  It is proposed to introduce additional power class for NR band in NSA band combination, similar to the manner as that for E-UTRA in RAN2 specification.