## Slide 1: 3GPP TSG RAN Meeting #88e RP-20xxxx Electronic Meeting, June 29 - July 3, 2020
Title: Final proposal of FR2_fallback
Source: Nokia (moderator)

## Slide 2: Scope of the [FR2_fallback] email discussion
Goal: Find a way forward on FR2 fallback. We shall not return this discussion to the WGs, but aim to make a decision at this RAN plenary, and approve all necessary CRs.
Input contributions covered: RP-201199, RP-200875, RP-201035

## Slide 3: Proposal for RAN#88e approval
All fallback combinations of an indicated CA combination are implicitly supported by a UE
  Hence, RAN2 signalling will not be changed
Relaxation of tests/requirements of fallback combinations, which includes FR2 intra-band CA combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination, are to be approved at RAN#89
  A terminal which supports a higher order CA or DC combination, which includes FR2 intra-band CA combinations with multiple subblocks, where at least one of the subblocks consists of a contiguous CA combination, shall conform to the requirements of the higher order combination and support the fallbacks without additional requirements for the fallback combination.