## Slide 1: Views on Rel-17 RAN4 package of non-spectrum related items
Qualcomm Incorporated
3GPP TSG-RAN Meeting #89e
Online, September 14 – 18, 2020
RP-201691
Document for: Approval

## Slide 2: Introduction
Rel.17 RAN4 non-spectrum package is up for approval in RAN#89e
Different proposals have been under e-mail discussion since RAN#88e
We present our view on what items should be prioritized for approval
  Items listed in the slides present our list of priorities, all could be approved with careful scoping

## Slide 3: General principles
Priority should be given to proposals that have bigger eco-system impact
  Approval of a bigger work item that opens-up new use cases should be prioritized over minor enhancements that have little system performance impact
The RRM session has seen the highest overload in recent years, hence a careful scoping of the related projects is highly desirable
  Avoid small items that start with a “study phase” (the benefit is likely very limited if a study is needed)

## Slide 4: UE RF Related Scope
RF FR1
  2Tx RF enhancements should be clearly scoped based on the outcome of Rel.16
    Rel.16 discussion on some items (e.g. Tx Div) is not yet concluded, objectives might have to be clarified in next plenaries
  Include per layer Tx EVM for Uplink MIMO
RF FR2
  CA enhancements should be based on band combinations explicitly requested by operators
  UE calibration gaps:
    performance gain should be first quantified and, if clear gains are shown, requirements should be defined with a clear side conditions
      E.g. output power is increased by X dB if gaps with Y periodicity are given to the UE

## Slide 5: RRM Related Scope
FR2 High Speed Trains
  Work should start with a study on the development scenario to determine the mobility requirements
FR1 High Speed Trains enhancements for CA
  Other enhancements should be de-prioritized
Measurement gaps
  Network controlled small gaps (NCSG) and burst gap pattern – little impact expected due to re-use of LTE solution
  Pre-configured gaps per BWP – little impact because only signaling changes are needed (impact on RAN4 requirements only at transitions)
  Multiple gap patterns configured simultaneously
RRM Enhancements
  SRS antenna port switching requirements
  Inter-RAT gapless measurements for LTE->NR and NR->LTE measurements
  HO with PSCell
  Idle mode requirement for SMTC2-LP

## Slide 6: BS related scope
RF Repeaters
  Multiple operators commented that this is needed as soon as possible for deployments
  Updated proposals to define RF requirements for “traditional repeaters” and study smart enhancements in parallel
DL 1024 QAM

## Slide 7: Demod
8 Rx requirements
  Aligns NR to LTE and work should be straightforward based on LTE

## Slide 8: OTA
TRP/TRS for FR1
OTA FR2 Dynamic testing
  3GPP is developing many advanced schemes that cannot be tested with current test setups
The industry needs requirements and testing solutions to verify “the real performance” of devices