## Slide 1
Study on AI based PHY layer enhancement for Rel-18
3GPP TSG-RAN WG Meeting #90-e
e-Meeting, December 7th–11th, 2020
Agenda Item: 9.12
Document for: Discussion & Decision
RP-202650

## Slide 2
Motivation of AI based PHY enhancement
Independent optimization for modules dependent on each other
E.g., Independent optimization for DL channel acquisition and DL precoding;
Linear sub-optimal algorithms and solutions for non-linear problems
E.g., Linear channel estimation for non-linear parameter estimation problems
Performance degradation with practical impairments or restrictions
E.g., EVM degradation and increased unwanted emission when approaching saturated output power due to PA non-linearity;
Non future-proof design without enough flexibility to conduct scenario specific optimization/evolution
E.g., Performance degradation with type I/II codebook for irregular antenna array in space limited scenarios;
E.g., Complicated (if not impossible) retuning of system parameters to adjust for evolving traffic/environment
Joint design of several modules could be easily done using AI
AI solutions could obtain near-optimal solutions for non-linear problems
Modeling of practical impairments becomes possible with AI
PHY layer design based on neural network provides the possibility to continuously evolve for various scenarios
  AI is a powerful tool to address challenges for PHY designs
  Limitations of current design in PHY

## Slide 3
Motivation of AI based PHY enhancement
  AI based PHY is feasible using chipset in current mobile phone :
    The capacity of one typical NPU used in current mobile phone is 8T operations (OPs) per second.
    The complexities of typical AI networks are listed in the below table and it is seen that the complexity of AI based PHY is already affordable.
 | Complexity (OPs) | Ratio of capacity of the typical chipset in 1 second
Inception V2 | 4.1G | 5.1e-4
Inception V3 | 12G | 1.5e-3
CaffeNet | 724M | 9.1e-5
GoogleNet | 2G | 2.5e-4
MobileNet | 1.15G | 1.4e-4
AI network for DMRS in the slides | 222M | 2.8e-5 (2.8e-2 in 1ms)
AI network for CSI feedback in the slides | 8.9M | 1.1e-6 (1.1e-3 in 1ms)
AI network for beam management in the slides | 544K | 6.8e-8 (6.8e-5 in 1ms)
AI for channel prediction in the slides | 7.3M | 9.1e-7 (9.1e-4 in 1ms)

## Slide 4
AI based DMRS channel estimation
  The problem of DMRS channel estimation is non-linear, and then winner filter based traditional linear algorithm is not optimal.
  Using near-optimal AI network, only 25% DMRS overhead is needed with time information.
AI
Channel on DMRS resources
Channel on all resources
With DMRS signal
Without DMRS signal
Method | MSE
Traditional algorithm with 1 slot channel estimation | 7.9e-3
AI network with 1 slot channel estimation | 4.85e-3
AI network with 10 slots joint channel estimation but totally 25% DMRS overhead | 5.69e-3
Parameters：LLS, SNR 10dB, UE speed 3km/h, TDL-C 300ns, 3.5G Hz, 1 gNB antenna, 1 UE antenna, 20 RBs. DMRS takes 6 subcarriers in 1 RB and 1 symbol in 1 slot.

## Slide 5
AI based CSI feedback
  AI network is not limited to certain restrictions of current codebook design.
  For low overhead case, 30% Tput gain is achieved using AI, compared to NR specified solutions.
Parameters：SLS, UMi 38.901, 7 cells, 3 sectors for each cell, UE speed 3km/h, carrier frequency 3.5 GHz, 32 gNB antenna ([Mg Ng M N P] = [1 1 2 8 2]), 4 UE antenna ([Mg Ng M N P] = [1 1 2 2 2]), 52 RBs. The overhead of PMI is 58 bits.
Method | Spectrum efficiency (bit/s/Hz)
NR specified solution | 6.41
AI | 8.28
AI encoder
AI decoder
UE side
gNB
CSI-RS channel estimation
Binary bits（PMI）
Recovered Channel Information

## Slide 6
AI on CSI-RS overhead reduction
  Full channel characteristic could be learnt by AI to reduce the CSI-RS overhead.
  Using 50% CSI-RS overhead, AI based CSI-RS compression could achieve better throughput than traditional algorithm with 100% CSI-RS overhead, in low SNR region.
Parameters：LLS, SNR -8~0dB, UE speed 3km/h, / CDL-C 300ns, carrier frequency 3.5G Hz, 128 gNB antennas, 64 CSI-RS ports, 4 UE antennas, 52 RBs..
AI
Full antenna ports
Less CSI-RS ports

## Slide 7
AI based fast beam selection
  Measure small number of beam pairs, and use AI to estimate qualities of all beam pairs.
  Compared to the measurement of 32 beam pairs in non-AI method, with AI-based methods UE only needs to measure 8 beam pairs hence reducing the number of measurements by 75%, expediting overall beam management process and reducing power consumption
Parameters：SLS, UMi 38.901, 7 cells, 3 sectors for each cell, UE speed 3km/h, carrier frequency 30GHz, subcarrier spacing 120KHz, 64 gNB antenna ([Mg Ng M N P] = [1 1 4 8 2]), 16 UE antenna ([Mg Ng M N P] = [1 1 2 4 2]), 52 RBs. L1-RSRP based beam selection method, 32 gNB beams and 16 UE beams.
AI
Qualities of selected beam pairs
Estimated qualities of all beam pairs
Chart: Number of measured beam pairs
| 2 | 4 | 8 | 16 | 32
Non-AI | 10.04 | 6.73 | 3.58 | 2.37 | 1.3
AI | 9.92 | 4.06 | 1.27 | 0.6 | 0.19

## Slide 8
AI based channel prediction
  Using the channel information measured from previous RS, AI-based mechanism could predict the future channel information very well.
  About 20% Tput gain is achieved by AI based channel prediction for speed 30km/h and single user scheduling.
Case | NMSE | 
 | Speed 3km/h | Speed 30km/h
No channel prediction | 0.15 | 1.6
AI with information of 2 periods | 2.5e-8 | 2.6e-7
AI with information of 4 periods | 3.3e-9 | 4.2e-8
AI with information of 6 periods | 7.9e-10 | 1.9e-8
AI with information of 8 periods | 5.0e-10 | 5.6e-9
AI with information of 10 periods | 3.3e-10 | 4.2e-9
Parameters：LLS, UE speed 3km/h or 30km/h, CDL-C 300 ns, carrier frequency 4G Hz, 32 gNB antennas, 2 UE antennas, 1 RB, maximum 1 layer, RS period 10 slots. No noise is considered.
Channel information of latest N periods
Predicted channel information
AI

## Slide 9
AI based DL CSI acquisition from SRS
  Compared to non-AI method, AI provides considerable gain with similar performance
    75% SRS overhead reduction
    6dB power reduction
AI
SRS
DL precoding
Case | MSE to ideal precoding
Comb2 SRS without AI | 0.12
Comb8 SRS without AI | 0.28
Comb8 SRS with AI | 0.14
Parameters：LLS, SNR 0dB, UE speed 3km/h, CDL-B 100 ns, carrier frequency 3.5G Hz, 4 gNB antennas, 2 UE antennas, 12 RB, maximum 1 layer. No power boosting for Comb8 SRS.

## Slide 10
AI based positioning
  InF-DH is typical scenario for I-IoT discussion, but in this scenario desired positioning accuracy is not achieved by Rel.16 based solutions (UTDOA/OTDOA/AOA/RTT, etc) as shown below.
  Clutter parameters of InF-DH are even modified.

## Slide 11
AI based positioning
Accuracy (m)
  Compared to Rel.16 solutions, AI based solutions could improve the accuracy dramatically at least from the following two aspects
    To combat NLOS in DH scenarios
    To combat synchronization error between different TRPs
Parameters：Deployment and channel model is based on current Rel-17 Positioning item discussion. InF-DH is focused..

## Slide 12
Potential application areas for AI in PHY layer
  Based on preliminary evaluations, application of AI to enhance PHY layer performance is promising.
  The following areas could be studied in Rel-18 for potential application of AI in PHY layer:
    Hardware impairments compensation, e.g., for PA non-linearity
    (Joint) optimization of one or more the following:
      RS transmission and estimation, including DMRS/SRS/CSI-RS, etc.
      CSI feedback, including application channel prediction
      Precoding strategy
    Mobility enhancement, including enhancement on intra-cell beam management and inter-cell mobility optimization
    Positioning enhancement

## Slide 13
THANK
YOU