## Slide 1: Views on Rel-17 RAN4-led non-spectrum WIs and SIs
MediaTek Inc.
3GPP TSG RAN#90E RP-202692
December 2020 Agenda Item 9.1.5

## Slide 2: Introduction
RAN#89e: RAN4-led non-spectrum WI/SI agreed
  NR_RF_FR1_enh ‒ NR_RF_FR2_req_enh2
  NR_RRM_enh2 ‒ NR_MG_enh
  NR_demod_enh2-Perf ‒ NR_DL1024QAM_FR1
  NR_HST_FR1_enh ‒ NR_HST_FR2_enh
  FS_NR_eff_BW_util
RAN#89e Action: WI/SI scope adjustment possible at RAN#90e
After RAN#89e: Misc. email threads for potential new Rel-17 RAN4-led WI/SI
  NR Repeaters
  ATG
  OTA
  EMC
.
MediaTek views in the following slides

## Slide 3: Rel-17 RAN4-led non-spectrum WI and SI MediaTek views
Agreed WI/SI | MediaTek View
NR_RF_FR1_enh | RAN1 effort is expected due to more complicated scenarios than Rel-16. Add RAN1 TU. Add one new objective for DC location reporting
NR_RF_FR2_req_enh2 | Keep current scope
NR_RRM_enh2 | 1.5 TU per-meeting. Current objectives do not demand a high workload. At most 2 additional objectives can be considered. Suggestion: Dedicated engine for CSI-RS measurement, CMTC for CSI-RS measurement
NR_MG_enh | 1 TU per-meeting. At most 1 additional objective can be considered. Suggestion: Inter-RAT/inter-freq NR measurement without gaps for LTE SA and MR-DC
NR_demod_enh2-Perf | Keep current scope 8Rx to be introduced in a separate WI due to impact on RF (REFSENS) and RRM (RLM)
NR_HST_FR1_enh | Keep current scope
NR_HST_FR2_enh | Keep current scope
NR_DL1024QAM_FR1 | Keep current scope
FS_NR_eff_BW_util | Keep current scope

## Slide 4: New Rel-17 RAN4-led non-spectrum WI and SI MediaTek views
Agreed WI/SI | MediaTek View
NR Repeaters | Support Complementary tool to resolve known coverage issues with NR (esp. FR1 TDD, and FR2) Shall be transparent to UEs on the field Rel-17 RAN4 WI: Basic AF repeater for FR1 FDD; and Rel-17 RAN4-led study with follow-up normative work: Smart Repeater for FR1 TDD and FR2 Unless scope clear at RAN#90, initial task to determine in Q1 exact scope, objectives and workload (RAN4, RAN1)
ATG | Support, however Coexistence scenarios to be further clarified (adjacent channel and co-channel) RRM and Demod work to be started later in order to leverage NTN outcome
OTA | FR1: Support FR2: Multiple FR2 OTA-related WI and SI are ongoing in RAN4. Relation and dependency to other WI/SI to be clarified.
EMC | Neutral

## Slide 5: NR_RF_FR1_enh MediaTek view: max one additional objective
DC location reporting for intra-band UL CA
Motivation
  Leftover in Rel-16 discussion
  Beneficial to both network and UE in improving UL decoding performance as well as to test equipment for accurate measuring of UL signal performance.
Recommended objective
  DC location reporting for intra-band UL CA [RAN4]
    Identify all factors to be considered for DC location reporting for more than 2 UL CCs [RAN4]
    Conclude on potential advanced methods to reduce the amount of signalling overhead [RAN4]
    Depending on the conclusion, implement the corresponding L1 procedure or RRC signaling [RAN1, RAN2]

## Slide 6: NR_RRM_enh2 MediaTek view: max two additional objectives
CMTC for CSI-RS L3 measurement
Motivation
  A clear time domain restriction CSI-RS based L3 measurement is missing for both UE to schedule the measurement among different frequency layers and for network to expect the UE behavior.
Recommended objective
  CMTC for CSI-RS L3 measurement [RAN4, RAN2]
    RRM requirement based on CMTC for CSI-RS L3 measurement
    Signaling design for CMTC of CSI-RS L3 measurement
Dedicated CSI-RS measurement engine
Motivation
  To address different and advanced UE implementation to perform parallel SSB and CSI-RS based L3 measurement
Recommended objective
  Dedicated CSI-RS measurement engine [RAN4, RAN2]
    RRM requirements for UEs with dedicated CSI-RS engine [RAN4]
    UE capability for UEs with dedicated CSI-RS engine [RAN2]

## Slide 7: NR_MG_enh MediaTek view: max one additional objective
Inter-RAT/inter-frequency NR measurement without gaps for LTE SA and MR-DC
Motivation
  No RRM requirement for NR gapless measurement in LTE SA or in MR-DC.
  Gap is always provided after MR-DC is configured, which may result in unnecessary performance lost
Recommended objective
  Inter-RAT/inter-frequency NR measurement without gaps for LTE SA and MR-DC
    Identify gapless scenario and specify RRM requirement [RAN4]
    Define gapless capability reporting [RAN2, RAN4]
    The objective does not apply to LTE measurement targets