## Slide 1
3GPP TSG RAN Meeting #91e RP-210319
Electronic Meeting, Mar. 22-26, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.7.27
Views on WID scope for Rel-17 RedCap

## Slide 2
  In RAN#90e meeting, a new WID on support of reduced capability NR devices was approved in [RP-202933] with the following scopes. The highlighted parts are to be revisited in RAN#91e
Background
Specify support for the following UE complexity reduction features [RAN1, RAN4]: Reduced maximum UE bandwidth: Maximum bandwidth of an FR1 RedCap UE during and after initial access of 20 MHz is supported. The possibility of, and any associated conditions for, optional support of a wider bandwidth up to 40MHz after initial access for this case will be further discussed at RAN#91e. Maximum bandwidth of an FR2 RedCap UE during and after initial access is 100 MHz Reduced minimum number of Rx branches: For frequency bands where a legacy NR UE is required to be equipped with a minimum of 2 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE is 1. The specification also supports 2 Rx branches for a RedCap UE in these bands. For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE will be decided at RAN#91e; hence no specific work for these frequency bands will be done before RAN#91e. Maximum number of DL MIMO layers: For a RedCap UE with 1 Rx branch, 1 DL MIMO layer is supported. For a RedCap UE with 2 Rx branches, 2 DL MIMO layers are supported. Relaxed maximum modulation order: Support of 256QAM in DL is optional (instead of mandatory) for an FR1 RedCap UE. No other relaxations of maximum modulation order are specified for a RedCap UE. Duplex operation: HD-FDD type A with the minimum specification impact (Note that FD-FDD and TDD are also supported.) Specify higher layer support of enhancements listed above [RAN2, RAN1]. Details are to be refined at RAN#91e taking the outcome of the RedCap SI into account, and work on this objective shall start after RAN#91e: Specify definition of RedCap UE type(s) including set(s) of L1 capabilities for RedCap UE identification and for constraining the use of those RedCap L1 capabilities only for RedCap UEs, and preventing RedCap UEs from using capabilities not intended for RedCap UEs including at least carrier aggregation, dual connectivity and wider bandwidths. Specify functionality that will enable RedCap UEs to be explicitly identifiable to networks and allow operators to restrict their access if desired. Specify necessary updates of UE capabilities (38.306) and RRC parameters (38.331). Specify RAN4 core requirements for the above.

## Slide 3
On number of Rx antennas
    For device types with form factor limitation (e.g. wearables), the performance gain by 2Rx is insignificant compared to 1Rx due to high antenna correlation (see RP-210320 for more details), however, the implementation challenging is high.
    As concluded in the study, no coverage issue in FR1 for 1Rx UE for 4GHz with typical gNB PSD (33dBm/MHz) and any other FR1 TDD bands
Proposal 1:
  For frequency bands where a legacy NR UE is required to be equipped with a minimum of 4 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE is 1. The specification also supports 2 Rx branches for a RedCap UE in these bands.
  No Redcap specific coverage recovery solutions are to be specified in Rel-17. Redcap UEs leverage the coverage enhancement solutions specified in other WIs (e.g. CE WI)
On Redcap UE BW
  For device types with form factor limitation, 40MHz BW capability is required to support 150Mbps peak data rate (40MHz BW, single layer, 64QAM)
  Proposal 2:
  Maximum bandwidth of an FR1 RedCap UE during and after initial access of 20 MHz is supported. 40MHz channel bandwidth after initial access is optionally supported.
RAN1 objectives on #Rx and BW

## Slide 4
In SI phase UE type definition for RedCap UEs and categorization of RedCap capabilities were discussed and summarized in TR 38.875. It was agreed and recommended that as a baseline, the existing UE capability framework is used to indicate the capabilities of RedCap UEs.
Considering the use cases and corresponding requirements are quite diverse for RedCap devices, we think two UE types/categories should be defined for RedCap devices to cover various use cases: high-end and low-end devices.
  The final categorization of capabilities into the studied categories depends on the exact capabilities applicable to RedCap UEs, to be defined during the WI phase.
Regarding how can the network be able to control that the RedCap UEs are only used for the intended use cases, several options were identified and summarized in TR 38.875. The down selection should be discussed in WI phase.
  At least for device type identification and possibly for constraining the use of reduced capabilities, the network needs to know whether the UE is RedCap UE or not.
Proposal 3: Include the following scope for identification and access restriction in RedCap WID
  Specify functionality that ensures Redcap UEs are only used for the intended use cases [RAN2]
RAN2 objectives - UE type and constraining

## Slide 5
Early indication for RedCap in Msg1, Msg3, MsgA, or in a later message have been studied and analysis in SI phase. It was agree that the necessity of early indication depends on the need for the network to know whether the UE accessing the system is a RedCap UE during the initial access, e.g. depending on the need of coverage recovery, different scheduling of RedCap UEs, or additional access restrictions.
  Actually, during RAN2 discussion, there is clearly majority think it is not needed from RAN2 perspective to identify RedCap UEs during Msg.1 and Msg.5.
  If the network allows RedCap UEs (supporting lower BW than the initial BWP of the cell) camping on a cell, it should be up to network implementation to schedule Msg4/5 with the BW restriction of RedCap UE. Thus, there is still no need to identify RedCap UEs in Msg.3
  Meanwhile, there is no need to reject part of RedCap UEs in addition to SI indicated cell barring and UAC mechanism, as UAC could be reused for access control.
Regarding access control of RedCap UEs in RAN, different mechanisms have been studied and analysis:
  System information indication to indicate whether a RedCap UE can camp on the cell or not.
  Unified access control should be applied to RedCap UEs, e.g. Different Access Identities/Categories can be used for different RedCap UE types.
Proposal 4: Include the following scope for identification and access restriction in RedCap WID
  Specify functionality that will enable RedCap UEs to be explicitly identifiable to networks and allow operators to restrict their access if desired. [RAN2, RAN1], considering following mechanisms:
    System information indication to indicate whether a RedCap UE can camp on the cell or not.
    Unified access control should be applied to RedCap UEs, e.g. Different Access Identities/Categories can be used for different RedCap UE types.
RAN2 objectives - identification and access restriction

## Slide 6
Power saving is very important for most of Redcap use cases
For eDRX:
  In SI phase, the upper and lower bound of extended DRX cycles were discussed. And the mechanisms for extended DRX were also initially discussed.
  Meanwhile, the simulation results summarized in TR 38.875 shows the significant power saving gain for eDRX. But it is based on the assumption that UEs are not required to perform RRM on serving cell outside PTW. Thus, this part should be further discussed in RAN4 in WI phase.
  For RRM relaxation
  In SI phase, RRM relaxation for RedCap UEs has been studied. The potential enhancement on RRM relaxation for neighboring cells in idle/inactive mode, and the methods on RRM relaxation for neighboring cells in connected mode were discussed and captured in TR 38.875.
  Meanwhile, the simulation results summarized in TR 38.875 shows that significant power saving gain (e.g. 13%~25%) for RRM relaxation for neighboring cells.
Proposal 5: Include the following scope for power saving in RedCap WID
  Specify UE power saving and battery lifetime enhancement for reduced capability UEs in applicable use cases [RAN2, RAN4]:
    RRM relaxation for neighboring cells in RRC Idle/Inactive and Connected mode under network control
    Extended DRX for RRC Inactive/Idle mode, unless RAN4 indicates such eDRX value requires UE to perform RRM on serving cell outside PTW
RAN2 objectives - UE power saving features

## Slide 7
Specify support for the following UE complexity reduction features [RAN1, RAN4]:
  Reduced maximum UE bandwidth:
    Maximum bandwidth of an FR1 RedCap UE during and after initial access of 20 MHz is supported. The possibility of, and any associated conditions for, optional support of a wider bandwidth up to 40MHz after initial access for this case will be further discussed at RAN#91e. 40MHz channel bandwidth after initial access is optionally supported.
    Maximum bandwidth of an FR2 RedCap UE during and after initial access is 100 MHz
  Reduced minimum number of Rx branches:
    For frequency bands where a legacy NR UE is required to be equipped with a minimum of 2 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE is 1. The specification also supports 2 Rx branches for a RedCap UE in these bands.
    For frequency bands where a legacy NR UE (other than 2-Rx vehicular UE) is required to be equipped with a minimum of 4 Rx antenna ports, the minimum number of Rx branches supported by specification for a RedCap UE will be decided at RAN#91e; hence no specific work for these frequency bands will be done before RAN#91e is 1. The specification also supports 2 Rx branches for a RedCap UE in these bands.
Specify higher layer support of enhancements listed above [RAN2, RAN1].
  Specify definition of RedCap UE type(s) including set(s) of L1 capabilities for RedCap UE identification and for constraining the use of those RedCap L1 capabilities only for RedCap UEs, and preventing RedCap UEs from using capabilities not intended for RedCap UEs including at least carrier aggregation, dual connectivity and wider bandwidths. [RAN2, RAN1]
  Specify functionality that ensures Redcap UEs are only used for the intended use cases [RAN2]
  Specify functionality that will enable RedCap UEs to be explicitly identifiable to networks and allow operators to restrict their access if desired, considering following mechanisms: [RAN2, RAN1]
    System information indication to indicate whether a RedCap UE can camp on the cell or not.
    Unified access control should be applied to RedCap UEs, e.g. Different Access Identities/Categories can be used for different RedCap UE types.
  Specify UE power saving and battery lifetime enhancement for reduced capability UEs in applicable use cases [RAN2, RAN4]:
    RRM relaxation for neighboring cells in RRC Idle/Inactive and Connected mode under network control
    Extended DRX for RRC Inactive/Idle mode, unless RAN4 indicates such eDRX value requires UE to perform RRM on serving cell outside PTW
  Specify necessary updates of UE capabilities (38.306), RRC parameters (38.331), and high layer procedure for corresponding functionalities listed above.
WID objective update - Proposals