## Slide 1: Conclusion of [RAN93e-R18Prep-02] UL enhancements
Moderator (NTT DOCOMO, INC.)
3GPP TSG-RAN Meeting #93-e
Electronic Meeting, September 13-17, 2021
Agenda Item: 9.0.1
RP-211652

## Slide 2
High-level description after refinement based on the email discussion
Uplink enhancements, with the following skeleton of the possible objectives:
  Study and if necessary specify >4 Tx UL operation, e.g., for CPE/FWA/vehicle/Industrial devices [leading WG: RAN1]
  Specify enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation, potentially including fast UL panel selection, separate UL timings/power controls for different panel/TRP and/or simultaneous multi-panel UL transmission [leading WG; RAN1]
  Study and if necessary specify frequency-selective precoding, mainly targeting devices with >=4 Tx [leading WG: RAN1]
  Specify further coverage enhancements including PRACH enhancement for FR2 e.g., PRACH repetition with same or different beams [leading WG: RAN1]
  Study and if necessary specify power domain enhancements e.g., dynamic power aggregation [leading WG: RAN4 or RAN1]
  Potentially specify other UL enhancements e.g., enhancement for multi-carrier UL operation, enhancements for DFTS-OFDM, enhancement for UL CW mapping [leading WG: RAN1]
General observation on UL enhancements
All companies would agree that “UL enhancement” can be considered as one of the key topics for Rel-18
There is a concern on potential too large scope for the UL enhancement, and hence further discussion on prioritization among example areas would be necessary as well as narrowing down the scope of each example area

## Slide 3
Controversial (FFS) points based on the email discussion
  For >4 Tx UL operation,
    FFS: whether only some listed example device types are targeted or even other device types are also targeted
    FFS: target frequency range
    FFS: RAN4 as secondary WG
  For enhanced multi-panel uplink operation and/or enhanced multi-TRP uplink operation,
    FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
    FFS: enhancements are based on Rel-17 unified TCI framework
    FFS: target frequency range
    FFS: RAN2/4 as secondary WG
  For frequency-selective precoding,
    FFS: whether this example area can be generalized to enhanced uplink precoding
    FFS: target frequency range and target devices
    FFS: RAN4 as secondary WG
  For further coverage enhancement and power domain enhancement
    FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
    FFS: other coverage enhancement e.g., DMRS-less PUCCH
  For other potential UL enhancements
    FFS: further clarification and narrowing down of the scope for this example area based on listed example scopes as starting point
    FFS: other potential scope, e.g., enhancement for UL dense deployment