## Slide 1
Agenda Item: 9.0.3
Source: Samsung
Title: Sidelink relay enhancement in Rel-18
Document for: Discussion and Decision
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 – 17, 2021
RP-211800

## Slide 2: Motivation
NR based sidelink relay is being specified under Rel-17 NR SL relay WID which supports UE’s coverage extension toward network.
  The NR sidelink relay covers various applications for public safety, V2X and commercial use cases.
Support of UE-to-UE coverage extension is necessary in Rel-18.
  UE-to-UE (U2U) relay can extend sidelink coverage.
  This U2U relay is useful especially for public safety with no Uu coverage.
Remote UE’s service continuity in U2N relay needs enhancement in Rel-18.
  In Rel-17 U2N relay, AS layer service continuity is supported limitedly within the same gNB.
  Service continuity should be supported for Remote UE’s mobility scenarios between different gNBs including indirect to indirect mobility.
UE1
UE2
U2U Relay
PC5
PC5
UE2
Coverage
UE1
Coverage

## Slide 3: Key Features: UE-to-UE Relay (Primary WG: RAN2)
Single-hop is prioritized
U2U relay discovery mechanism
U2U relay (re)selection mechanism including sidelink measurement
U2U relay UE and remote UE authorization mechanism
※Note that the features above can be defined for L3 relaying and L2 relaying if both relay types are considered.
If L2 relaying is considered, L2 specific feature can be specified as follows:
  PC5 adaptation layer design for L2 U2U relay
  Control plane procedures if any RAN impact is identified by SA2.

## Slide 4: Key Features: R17 Leftovers for Service Continuity (Primary WG: RAN2)
L2 U2N relay specific service continuity mechanisms for intra-gNB case
  Indirect (via a first Relay UE) to indirect (via a second Relay UE) mobility scenario within the same gNB
L2 U2N relay specific service continuity mechanisms for inter-gNB cases
  Direct to indirect mobility scenario between gNBs
  Indirect to direct mobility scenario between gNBs
  Indirect to indirect mobility scenario between gNBs
UE1
UE1
gNB A
gNB B
Relay UE
Uu
Uu
PC5
move
UE1
UE1
gNB A
gNB B
Relay UE
Uu
Uu
PC5
move
UE1
gNB B
Relay UE 2
Uu
PC5
gNB A
Relay UE 1
Uu
PC5
UE1
move