## Slide 1: Discussion on UE Aggregation
CMCC
3GPP TSG RAN Meeting #93e RP-211992
Electronic Meeting, September 13 - 17, 2021
Agenda item: 9.0.3

## Slide 2: Motivation
AR/VR
Video for Remote Monitoring
Drone with live video
The motivation of this SI is to investigate how to address the issue of the shortage of UL UE transmission power in 5G via UE aggregation mechanism:
  In compare to LTE, various type services required the wide UL bandwidth requirement is increasing and becomes pervasive in 5G network
    e.g. AR/VR devices, live video from UAV, etc.
  In this case, the bottleneck of supporting the applications with wide UL bandwidth on 5G terminals is the limited UL UE transmission power, e.g. 23dBm or 26dBm, especially at the edge area of a cell.
  Although some enhancement to eliminate the bottleneck has been adopted, e.g. SUL, super Uplink, it seems not sufficient to satisfy the demand.
  This is in particular useful in the case of the terminal with less size limitation
        UE aggregation will be feasible to extend the scale of aggregated UEs, i.e., the UE aggregation mechanism can easily increase the number of aggregated UEs and expandability effectively
        e.g. terminal equipped in the UAV, vehicle and assessment line for motion controller in the factory

## Slide 3: Motivations
Issue
  How to avoid the data disorder and data duplication during the data splitting between the aggregated UEs
Intention of the SI is to study the potential UE aggregation mechanism
  Which kind of L2 architecture can be utilized to aggregate more than one terminal to improve the UL throughput
  How to support the data lossless or minimized data loss during the session/packet switching amongst the aggregated terminals
Figure : L2 architecture of UE aggregation for UL TX power boosting

## Slide 4: SI OBJECTIVES
Identify and study potential UE aggregation mechanism, including [RAN2, RAN3]
  RRC management procedure to enable UE aggregation [RAN2]
  L2 architecture, functionalities and interfaces to allow aggregated UEs to receive control signalling/data in coordination mode, e.g. without data disorder or data duplication during the data splitting between the aggregated UEs [RAN2]
  Mobility of aggregated UEs with Service continuity [RAN3]

## Slide 5: Compared to relevant approaches
Regarding the concern about multi-path Relay mentioned by several companies:
                although the multi-path relay partially meets the UE aggregation requirement, however, the UE aggregation will not restrict the connection between UEs and will be feasible to extend the scale of aggregated UEs
                i.e. the UE aggregation mechanism can easily increase the number of aggregated UEs and expandability effectively, although dual UE aggregation can be studied in R18 as starting point.
                Hence, it is obviously more generic and bring more flexibility and expandability for the application of the mechanism than that of multi-path Relay.
In response to Comment - Contentious Points (Observation) summarized in the moderator's point on ": MP-TCP can perform similar aggregation so the justification is weak. Target scenario and motivation (what to achieve) and detailed reasons why is not clear. The impact may be unreasonably high in Rel-18.",
  however, as we know, MP-TCP is specified mainly in case of different RAT, e.g. WIFI and 5G, which is only restricted to one single UE.
  Additionally, TCP is not supported in all services.
  Moreover, the high layer cannot be aware of the condition of air interface and can neither appropriately allocate the radio resources according to the radio link condition, nor achieve the gain from the link adaptive

## Slide 6: Compared to relevant approaches
In response to the moderator's point on "compare with higher Power UE"
  since there is no normative limitation of UL transmission power on the aggregated UEs since the number of the aggregated UE can be flexibly extended
  the UE aggregation mechanism is sufficiently elastic to accommodate various UL bandwidth requirement of different applications,
In response to the moderator's point on "compare with application level solutions for aggregation"
  the existing application level solutions can be only supported in the special customized applications
  resulting in the application of UE aggregation can not be widely spread.

## Slide 7
Thank you!