## Slide 1
Discussion on network energy saving
3GPP TSG RAN Meeting #93-e RP-211994
Electronic Meeting, September 13 - 17, 2021
Agenda Item: 9.0.2
Source: CMCC

## Slide 2
Motivation
Power consumption of a 5G base station will be 3~4 times higher than LTE, due to 8 times TX/RX channels, 5 times bandwidth and larger transmission powers, leading to higher OPEX.
Standardization efforts have been given to UE power savings in Rel-15/16/17, network power consumption has not been the focus.
More efficient energy saving mechanism is needed to timely respond to the real-time traffic/UE distribution.
5G network has been widely deployed since 2019, with the increasing number of 5G gNBs, it is urgent for operators to reduce network energy consumption and maintain a sustainable 5G deployment
Power consumption Percentage of BS component
Power consumption Percentage of AAU components in difference load status
Fully loaded
30% loaded
empty load
Power Amplifier
Small signal
Digital IF
Power Module
Proposal 1: Enhancement of energy saving should be studied and followed by normative work in Rel-18

## Slide 3
Potential study areas
Study on modeling of network energy consumption
  Compare and make down selection of two modeling methods, namely absolute energy consumption metric and relative energy consumption metric
  Define different energy consumption states and values, including different sleep status, transition time, DL transmission and UL reception with different scaling factors in spatial domain/frequency domain/power domain, etc.
Study on evaluation methodology and scenarios
  The scenarios can be macro and micro deployment, FR1 can be high priority
  SLS can be used to evaluate energy saving gain of different solutions and the network/UE performance impact, solutions choice needs to be balanced
    Different UE traffic models and network traffic loads can be considered

## Slide 4
Potential study areas
Study the following potential network energy saving solutions :
  Network energy saving in spatial domain [RAN1]:
    Dynamic TX/RX on/off
    Dynamic RS ports adaption
    Potential CSI measurement/report enhancement
  Network energy saving in time domain [RAN1/2]:
    Dynamic network on/off to enable different sleep modes
      wake up signal design
    Periodic RS transmission adaptation, e.g., SSB/SIB/paging periodicity adaptation, partial beams on/off of SSB/SIB/paging
  Network energy saving in frequency domain [RAN1/2]:
    Power efficient CA/DC operation
  Network energy saving in power domain [RAN1]:
    Dynamic transmit power level adjustment
  UE assistance information [RAN2]:
    UE’s traffic, location, preference configuration, etc.
  Inter-node assistance information [RAN3]:
    Exchange the configuration or information of TX/RX number, periodic RS periodicity/beams, power, energy saving mode, etc.

## Slide 5
THANK YOU !