## Slide 1
3GPP TSG RAN 93e RP-212013
Electronic Meeting, Sep. 13th-17th, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.0.3
Enhanced support for collaborative Ues in Rel-18

## Slide 2
Motivation
  Trends of increasing wearable devices
  Trends of increasing IoT devices in home environment
  Trends of increasing IoT devices in small offices/factories
  Capability constraints, e.g., size, weight, power, cost
  Improve network capability, i.e., support large throughput without single point resource consumption
  Improve coverage with 5GS resource efficiency, i.e., improve reliability without resource consumption during the period of good condition, which is the most case
  Improve user experience, i.e., manage devices and communications in network style
  Collaborative UE(PIOT)
Motivations
Wearables （to C)
Office/Factory (to B)
Home (to C)

## Slide 3
  Collaborative UE(PIOT)
Considerations
There are three cases for Collaborative UE based on the RWS discussion, i.e., UE aggregation, Service switching and UE backup
  UE aggregation
    UL throughput improvement in coverage limitation case for UE aggregation
    UL transmission and DL reception can be separated from different UEs for UL boosting and power saving
  Service switching
    Enable fast service switching across UEs with no data loss
  UE backup
    Improved reliability and robustness for URLLC scenario while saving radio resources
UE aggregation
RAN based
Failed path
Switched path
Direct link
On-going CN media
5GS signaling
RAN based
Service switching
UE Backup
Observation: Similar CP and UP architecture for three cases if RAN based solution with PDCP as anchor is used
Notes: Requirements, use case, motivation from IEEE

## Slide 4
  Collaborative UE(PIOT)
SID Objectives
1 Determine the level of coordination between the UEs and the assumptions for the interconnect link (e.g. non-specified high-performance link). Determine if / to what extent the multiplicity of UEs is handledby / is visible to the Core Network / higher layers [RAN2];
2 Study UP operation and architecture, e.g. PDCP aggregation/split [RAN2];
3 Study mechanisms on AS CP coordination and handling for the multiple connections (e.g. Setup/Modification/Release procedures for the UE aggregation backup and mobility in coordination manner) [RAN2];
4 Study mechanisms on fast failure detection and fast recovery procedures [RAN2];
Proposal: We should study UE aggregation, service switching and UE back up together in one SI.

## Slide 5
  Annex
Based on Single UE with both 3GPP and non-3GPP registration;
Not all services support TCP, Traffic routing, splitting or switching based on MPTCP or ATSSS-LL functionality
High layer can not know the radio channel quickly.
Multi-path based on single UE’s MA PDU session with user planes on 3GPP access or non-3GPP access or both;
Some drawbacks for high layer aggregation and high power UE
It is hard to extend multiple UEs;
CAN NOT get adaptive gain from multiple leg
Some consumer devices do not support high power UE
High layer aggregation
High power UE