## Slide 1
3GPP TSG RAN 93e RP-212015
Electronic Meeting, Sep. 13th-17th, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.0.3
Enhanced support for multi-SIM devices in Rel-18

## Slide 2
Motivations:
  It is quite important to support dual RRC connection in both network A and network B. like the scenarios, we use the navigation in our smart phone in network A and receive a voice call from the network B. we indeed do not expect disconnect one of network.
  Interoperability issues have already emerged for dual-Tx/dual-Rx MUSIM devices, e.g.
    In Network A, UEA/USIM-A can report 2 Tx chain capability in UL when UEB/USIM-B is in RRC idle in Network B. If UEB goes back into RRC Connected, the MUSIM device has to tune away one Tx chain to UEB. If the Network A cannot adapt to the changes in UL ports, then Network A would not be aligned with the UE, resulting demodulation failure, or radio link failure
  Enhancement support for multi-SIM devices
Motivation and potential scope

## Slide 3
About 20 companies agreed the MUSIM should be enhanced in R18
Capability change and notification about Scell/SCG release are convergence
Some companies still thought Capability change of UE was not allowed, however no concrete arguments were provided why this should be disallowed.
  Enhancement support for multi-SIM devices
Discussion in pre-email discussion

## Slide 4
Potential objectives:
  Specify mechanism for UE staying in RRC_CONNECTED state simultaneously on both Network A and B (for MUSIM purpose) [RAN2, RAN4]:
    UE capability coordination/update with Network A of switching partial capability (e.g. Tx or Rx chains) from/to Network A. [RAN2, RAN4].
    UE-initiated request of SCell/SCG deactivation or release.[RAN2]
    RAT Concurrency: Network A is NR. Network B can either be LTE or NR.
    Applicable UE architecture: Dual-Rx/Dual-Tx
  Enhancement support for multi-SIM devices
potential scope