## Slide 1
Study on Further enhancement of multi-TRP
transmission for NR
ETRI
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 - 17, 2021
RP-212052

## Slide 2: Motivation
5G Advanced demands breakthrough technologies
  3GPP has successfully achieved 5G Requirements
  Rel-18 should be the starting point for new technologies
Increasing demand for user-centric communication services
  XR including AR/VR/MR would be the important 5G Advanced applications
  NR should support high-rate data transmission regardless of user location
Necessity of truly user-centric connectivity/network
  For ubiquitous services, cell-edge performance should be significantly increased
  NR still suffers from poor cell-edge performance
    The ratio of peak-to-edge rate is amounted to 200, according to 5G Requirements
NR should provide high performance consistently
  Multi-TRP transmission efficiently provides user-centric connectivity
  Cell-free massive MIMO can be introduced based on the multi-TRP transmission

## Slide 3: Technology
Cell-free massive MIMO
  Cell-free massive MIMO is a single cell Massive MIMO system with antennas distributed over a wide geographical area, which makes the joint channel from the TRPs to a user strongly spatially correlated
  Uses simultaneous data transmission over non co-located multiple antennas
  Supports higher data rate to all users regardless of geographic location
  Provides much wider coverage than co-located Massive MIMO
  Practical and useful implementation scheme in distributed multi-TRP architecture
  It is well-known for a promising candidate for 5G/6G
    [1] “Cell-Free Massive MIMO Versus Small Cells,” IEEE Transactions on Wireless Communications, 2017.
    [2] “The Road to 6G: Ten Physical Layer Challenges for Communications Engineers,” IEEE Communications Magazine, 2021.
    [3] 6G Flagship, “White Paper on Broadband Connectivity in 6G,” 6G Research Visions, 2020.

## Slide 4: Performance
Cell-free massive MIMO
  Cell-Free Massive MIMO has considerably improved performance with respect to a conventional small-cell scheme [1]
    Under uncorrelated shadow fading conditions, the cell-free scheme provides nearly fivefold improvement in 95%-likely per-user throughput over the small-cell scheme, and tenfold improvement when shadow fading is correlated.
  Cell-free massive MIMO requires massive TRPs
    Practical researches nowadays show the similar performance with smaller TRPs (e.g. 10x)
  Realises no cell-edge users
    Undesirable ‘edge-effect’ can be avoided
    Fairness among users can be improved
  Higher data rate for all users
    High multiplexing gain
    High array gain
    Energy efficiency

## Slide 5: Objective
Study Item Objective
  Feasibility study on the support of Cell-free massive MIMO feature
  Both FR1 and FR2
  FDD/TDD
    More focus on TDD to consider CSI feedback overheads.
  Downlink/Uplink
    More focus on downlink data transmission for video streaming services.
  Distributed MIMO architecture
    Non co-located multi-TRP deployments up to 64 TRPs.
  Coherent - Joint Transmission (C-JT)
    More focus on data transmission (PDSCH).
  Reuse NR eMBB framework as much as possible (including Rel-17 FeMIMO)
  Minimize UE modification